## Slide 1
ELEC 335 | Fall 2026
State, latches and flip-flops
Week 9 · Lecture 1
Chapter 6
Digital Logic Design
Textbook: Ch. 6 §§6.1–6.3, pp. 365–380
Notes: ELEC 335 | Lecture 15 | Week 9
Opening
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 6 §§6.1–6.3, pp. 365–380.
Companion animation: lesson-01.html
Opening question: When does stored information change?
Outcomes: Separate present state Q from next state Q⁺ | Compare a transparent latch with an edge-triggered flip-flop | Apply D, T, JK and SR characteristic rules

## Slide 2
L15 · READING MAP
Where this lecture sits in the course
Textbook: Ch. 6 §§6.1–6.3, pp. 365–380
ELEC 335 | L15 | Week 9
2
1
Textbook: Ch. 6 §§6.1–6.3, pp. 365–380
2
Interactive companion: Lesson 01, State, latches and flip-flops
3
After class: worked examples and practice in the HTML lesson
Preparation: read the named section, then use the worked slides to check each design step.
Notes: ELEC 335 | Lecture 15 | Week 9
Reading map
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 6 §§6.1–6.3, pp. 365–380.
Companion animation: lesson-01.html

## Slide 3
L15 · LEARNING OUTCOMES
Today's destination
Textbook: Ch. 6 §§6.1–6.3, pp. 365–380
ELEC 335 | L15 | Week 9
3
01
Separate present state Q from next state Q⁺
02
Compare a transparent latch with an edge-triggered flip-flop
03
Apply D, T, JK and SR characteristic rules
Course outcome: Flip-flops and sequential behavior
Notes: ELEC 335 | Lecture 15 | Week 9
Learning outcomes
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 6 §§6.1–6.3, pp. 365–380.
Companion animation: lesson-01.html
Separate present state Q from next state Q⁺
Compare a transparent latch with an edge-triggered flip-flop
Apply D, T, JK and SR characteristic rules

## Slide 4
L15 · BIG PICTURE
The question that organizes today
Textbook: Ch. 6 §§6.1–6.3, pp. 365–380
ELEC 335 | L15 | Week 9
4
When does stored information change?
Keep this question in view as the circuit models and examples develop.
Notes: ELEC 335 | Lecture 15 | Week 9
Guiding question
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 6 §§6.1–6.3, pp. 365–380.
Companion animation: lesson-01.html
Ask students for an initial answer: When does stored information change?

## Slide 5
L15 · PREREQUISITE BRIDGE
Start from what you already know
Textbook: Ch. 6 §§6.1–6.3, pp. 365–380
ELEC 335 | L15 | Week 9
5
✓
Combinational outputs depend on the current input values.
✓
A feedback path can preserve information from an earlier interval.
✓
A clock or enable determines when stored information may change.
Turn to a partner: explain one statement without reading it aloud.
Notes: ELEC 335 | Lecture 15 | Week 9
Prerequisite bridge
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 6 §§6.1–6.3, pp. 365–380.
Companion animation: lesson-01.html
Combinational outputs depend on the current input values.
A feedback path can preserve information from an earlier interval.
A clock or enable determines when stored information may change.

## Slide 6
L15 · VOCABULARY
Four words to make precise
Textbook: Ch. 6 §§6.1–6.3, pp. 365–380
ELEC 335 | L15 | Week 9
6
present state
the stored value before the controlling event
next state
the value stored after the controlling event
latch
storage controlled by an active level
flip-flop
storage sampled at an active clock edge
Use each term when explaining the circuit, table, or timing trace.
Notes: ELEC 335 | Lecture 15 | Week 9
Vocabulary
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 6 §§6.1–6.3, pp. 365–380.
Companion animation: lesson-01.html
present state: the stored value before the controlling event
next state: the value stored after the controlling event
latch: storage controlled by an active level
flip-flop: storage sampled at an active clock edge

## Slide 7
L15 · PLAIN-LANGUAGE MODEL
The reasoning sequence
Textbook: Ch. 6 §§6.1–6.3, pp. 365–380
ELEC 335 | L15 | Week 9
7
01
Name the present state and input.
02
Identify the active level or edge.
03
Apply the device rule, then hold the result until the next event.
When does stored information change?
Notes: ELEC 335 | Lecture 15 | Week 9
Plain-language model
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 6 §§6.1–6.3, pp. 365–380.
Companion animation: lesson-01.html
Name the present state and input.
Identify the active level or edge.
Apply the device rule, then hold the result until the next event.

## Slide 8
L15 · REFERENCE
The table to keep beside the method
Textbook: Ch. 6 §§6.1–6.3, pp. 365–380
ELEC 335 | L15 | Week 9
8
Device | Controls | Next-state behavior
D flip-flop | D | Q⁺=D at the active edge
T flip-flop | T | 0 hold; 1 toggle
JK flip-flop | J,K | 00 hold; 01 reset; 10 set; 11 toggle
Active-high SR latch | S,R | 00 hold; 01 reset; 10 set; 11 invalid
D, T and JK are clocked here. The basic SR device is a level-sensitive latch.
Notes: ELEC 335 | Lecture 15 | Week 9
Reference table
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 6 §§6.1–6.3, pp. 365–380.
Companion animation: lesson-01.html
Read all columns in the bit order shown. Ask students to predict one row before the worked example.

## Slide 9
L15 · STATE NOTATION
Q is present state; Q⁺ is next state
Textbook: Ch. 6 §§6.1–6.3, pp. 365–380
ELEC 335 | L15 | Week 9
9
Q
stored before
controlling event
→
Q⁺ (Q*)
stored after
Q⁺ is the value that will be stored next.
A flip-flop responds at an active clock edge; a latch responds during an active level.
Example: Q=0 and D=1 before a rising edge. At that edge, Q⁺=1; Q then holds 1 until the next edge.
Notes: ELEC 335 | Lecture 15 | Week 9
Present and next state
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 6 §§6.1–6.3, pp. 365–380.
Companion animation: lesson-01.html
Q is the stored bit just before an event. Q⁺, also written Q*, is its next value. For an edge-triggered D flip-flop, sample D at the active edge. The physical output settles after propagation delay and holds between edges. For a level-sensitive latch, a valid control level permits an update without a clock edge.

## Slide 10
L15 · D FLIP-FLOP
D copies the data input at the active edge
Textbook: Ch. 6 §§6.1–6.3, pp. 365–380
ELEC 335 | L15 | Week 9
10
D means data. A D flip-flop has one data input and one stored output Q.
Present Q | D at edge | Next Q⁺
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
Rule
Q⁺ = D
The old Q does not alter the copied value. Between edges, Q holds.
Example: Q=0, D=1 at a rising edge. The new Q is 1.
Notes: ELEC 335 | Lecture 15 | Week 9
D flip-flop
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 6 §§6.1–6.3, pp. 365–380.
Companion animation: lesson-01.html
The D input supplies the desired next-state bit. Sample D at the active edge; Q then updates after device propagation delay. Example: Q=0 and D=1 at the edge gives Q⁺=1. D can change between edges without changing Q.

## Slide 11
L15 · T FLIP-FLOP
T chooses hold or toggle at the active edge
Textbook: Ch. 6 §§6.1–6.3, pp. 365–380
ELEC 335 | L15 | Week 9
11
T means toggle. T=0 holds the stored bit; T=1 complements it.
Present Q | T at edge | Next Q⁺
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
Rule
Q⁺ = Q ⊕ T
A toggle changes 0 to 1 or 1 to 0. The output holds between edges.
Example: Q=1, T=1 at a rising edge. The new Q is 0.
Notes: ELEC 335 | Lecture 15 | Week 9
T flip-flop
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 6 §§6.1–6.3, pp. 365–380.
Companion animation: lesson-01.html
T=0 means no state change. T=1 requests a toggle, so Q⁺=Q⊕T. Example: Q=1 and T=1 gives Q⁺=0. T flip-flops are useful in counters, with the triggering edge specified.

## Slide 12
L15 · JK FLIP-FLOP
J and K choose hold, reset, set or toggle
Textbook: Ch. 6 §§6.1–6.3, pp. 365–380
ELEC 335 | L15 | Week 9
12
J is the set control and K is the reset control. Both are sampled at the active edge.
J | K | Command | Q⁺ if Q=0 | Q⁺ if Q=1
0 | 0 | hold | 0 | 1
0 | 1 | reset | 0 | 0
1 | 0 | set | 1 | 1
1 | 1 | toggle | 1 | 0
Equation: Q⁺=JQ′+K′Q. Example: Q=1, J=0, K=1 gives Q⁺=0.
Notes: ELEC 335 | Lecture 15 | Week 9
JK flip-flop
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 6 §§6.1–6.3, pp. 365–380.
Companion animation: lesson-01.html
J=1 alone sets Q. K=1 alone resets Q. J=K=0 holds. J=K=1 toggles. The controls are read at the active clock edge. From Q=1 with J=0 and K=1, Q⁺=0.

## Slide 13
L15 · SR LATCH
Set and reset control a basic SR latch
Textbook: Ch. 6 §§6.1–6.3, pp. 365–380
ELEC 335 | L15 | Week 9
13
S means set and R means reset. This table is for an active-high SR latch.
S | R | Command | Next Q
0 | 0 | hold | Q
0 | 1 | reset | 0
1 | 0 | set | 1
1 | 1 | invalid | undefined after release
A latch responds when S or R is asserted; it does not wait for a clock edge.
A clocked SR flip-flop samples similar requests at its edge. Always check the device and input polarity.
Notes: ELEC 335 | Lecture 15 | Week 9
Basic active-high SR latch
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 6 §§6.1–6.3, pp. 365–380.
Companion animation: lesson-01.html
For an active-high SR latch: 00 holds, 10 sets, 01 resets, and 11 is forbidden because the complementary outputs cease to be valid and the released state can be uncertain. Q may change as soon as a valid request propagates. A clocked SR flip-flop applies controls at the specified edge. An active-low NAND latch has different asserted levels; always check polarity.

## Slide 14
L15 · METHOD
A reliable procedure for exercises
Textbook: Ch. 6 §§6.1–6.3, pp. 365–380
ELEC 335 | L15 | Week 9
14
1
Identify the storage device, active level or edge, and initial state.
2
Mark the input value at every controlling event before computing Q⁺.
3
Use the characteristic rule one event at a time, then draw the held intervals.
Complete the table or trace, then verify the circuit one row at a time.
Notes: ELEC 335 | Lecture 15 | Week 9
Textbook exercise method
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 6 §§6.1–6.3, pp. 365–380.
Companion animation: lesson-01.html
Identify the storage device, active level or edge, and initial state.
Mark the input value at every controlling event before computing Q⁺.
Use the characteristic rule one event at a time, then draw the held intervals.

## Slide 15
L15 · WORKED EXAMPLE
Trace a D flip-flop
Textbook: Ch. 6 §§6.1–6.3, pp. 365–380
ELEC 335 | L15 | Week 9
15
Initially Q=0. D is 1 before edge 1, changes to 0 after that edge, and returns to 1 before edge 3. Find Q after three rising edges.
1
At edge 1, D=1, so Q⁺=1.
2
At edge 2, D=0, so Q⁺=0.
3
At edge 3, D=1, so Q⁺=1.
4
Between edges Q holds, even when D changes.
The sequence after the edges is 1, 0, 1.
Notes: ELEC 335 | Lecture 15 | Week 9
Trace a D flip-flop
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 6 §§6.1–6.3, pp. 365–380.
Companion animation: lesson-01.html
Prompt: Initially Q=0. D is 1 before edge 1, changes to 0 after that edge, and returns to 1 before edge 3. Find Q after three rising edges.
Steps:
At edge 1, D=1, so Q⁺=1.
At edge 2, D=0, so Q⁺=0.
At edge 3, D=1, so Q⁺=1.
Between edges Q holds, even when D changes.
Answer: The sequence after the edges is 1, 0, 1.

## Slide 16
L15 · CONCEPT
Two designs to distinguish
Textbook: Ch. 6 §§6.1–6.3, pp. 365–380
ELEC 335 | L15 | Week 9
16
D latch
Follows D while enable is active.
Holds when enable is inactive.
D flip-flop
Samples D at its active edge.
Holds between active edges.
Explain the difference using behavior and timing, then test one case.
Notes: ELEC 335 | Lecture 15 | Week 9
Concept comparison
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 6 §§6.1–6.3, pp. 365–380.
Companion animation: lesson-01.html
D latch | Follows D while enable is active. | Holds when enable is inactive.
D flip-flop | Samples D at its active edge. | Holds between active edges.

## Slide 17
L15 · INTERACTIVE COMPANION
Clock-edge laboratory
Textbook: Ch. 6 §§6.1–6.3, pp. 365–380
ELEC 335 | L15 | Week 9
17
D
→
D flip-flop
→
Q
Clock edge
Change the input between edges. Only the active edge updates these clocked devices. The asynchronous SR latch appears in Lesson 04.
Open lesson-01.html for the animated model and state-by-state controls.
Notes: ELEC 335 | Lecture 15 | Week 9
Interactive model
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 6 §§6.1–6.3, pp. 365–380.
Companion animation: lesson-01.html
Change the input between edges. Only the active edge updates these clocked devices. The asynchronous SR latch appears in Lesson 04.
Pause the laboratory between edges and change D twice. Ask whether Q follows.
Switch between D and T modes. Have students predict Q⁺ before pressing Clock.
Write Q and Q⁺ in separate columns throughout the lesson.

## Slide 18
ACTIVITY
L15
TEAM
TASK
Apply the method together
Given one D waveform and three rising clock edges, sketch both latch and flip-flop outputs. Mark the intervals when each output may change.
Identify the storage device, active level or edge, and initial state.
DELIVERABLE
Two timing traces with every controlling event labelled.
Textbook: Ch. 6 §§6.1–6.3, pp. 365–380
L15 | Week 9
ELEC 335 | Digital Logic Design
18
Notes: ELEC 335 | Lecture 15 | Week 9
Team activity
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 6 §§6.1–6.3, pp. 365–380.
Companion animation: lesson-01.html
Given one D waveform and three rising clock edges, sketch both latch and flip-flop outputs. Mark the intervals when each output may change.
Deliverable: Two timing traces with every controlling event labelled.

## Slide 19
L15 · GUIDED EXAMPLE
Try the first move before I do
Textbook: Ch. 6 §§6.1–6.3, pp. 365–380
ELEC 335 | L15 | Week 9
19
A JK flip-flop has Q=1, J=0 and K=1. Determine Q⁺.
YOUR FIRST MOVE
The control pair JK=01 requests reset.
Pause for 60–90 seconds. Write, then compare with a partner.
Notes: ELEC 335 | Lecture 15 | Week 9
Guided example
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 6 §§6.1–6.3, pp. 365–380.
Companion animation: lesson-01.html
Prompt: A JK flip-flop has Q=1, J=0 and K=1. Determine Q⁺.
First move: The control pair JK=01 requests reset.
Pause before showing the next slide.

## Slide 20
L15 · GUIDED SOLUTION
Now make every step visible
Textbook: Ch. 6 §§6.1–6.3, pp. 365–380
ELEC 335 | L15 | Week 9
20
1
The control pair JK=01 requests reset.
2
Substitute into Q⁺=JQ′+K′Q.
3
Q⁺=0·0+0·1=0.
Q⁺=0.
Notes: ELEC 335 | Lecture 15 | Week 9
Use a characteristic equation
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 6 §§6.1–6.3, pp. 365–380.
Companion animation: lesson-01.html
Steps:
The control pair JK=01 requests reset.
Substitute into Q⁺=JQ′+K′Q.
Q⁺=0·0+0·1=0.
Answer: Q⁺=0.

## Slide 21
L15 · MISCONCEPTION CLINIC
A tempting mistake to remove now
Textbook: Ch. 6 §§6.1–6.3, pp. 365–380
ELEC 335 | L15 | Week 9
21
TEMPTING CLAIM
A flip-flop follows D for the entire high clock level.
WHY IT FAILS
A clock edge is a sampling event, while a latch responds throughout its active level.
REPAIR
Mark the active edge and sample D only there.
Notes: ELEC 335 | Lecture 15 | Week 9
Misconception clinic
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 6 §§6.1–6.3, pp. 365–380.
Companion animation: lesson-01.html
TEMPTING CLAIM: A flip-flop follows D for the entire high clock level.
WHY IT FAILS: A clock edge is a sampling event, while a latch responds throughout its active level.
REPAIR: Mark the active edge and sample D only there.

## Slide 22
L15 · ONE-MINUTE CHECKS
Close the book: can you apply it?
Textbook: Ch. 6 §§6.1–6.3, pp. 365–380
ELEC 335 | L15 | Week 9
22
Q1
A T flip-flop has Q=1 and T=1. What is Q⁺?
Q2
A D latch has enable=1. D changes 0→1 before enable falls. What is Q just before enable falls?
Answer without notes, then compare your reasoning with the next slide.
Notes: ELEC 335 | Lecture 15 | Week 9
Practice questions
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 6 §§6.1–6.3, pp. 365–380.
Companion animation: lesson-01.html
Q1: A T flip-flop has Q=1 and T=1. What is Q⁺?
Hint: T=1 requests a toggle.
Answer: Q⁺=Q⊕T=1⊕1=0.
Q2: A D latch has enable=1. D changes 0→1 before enable falls. What is Q just before enable falls?
Hint: The latch is transparent during the active level.
Answer: Q=1, assuming D has settled. After enable falls, the latch holds 1.

## Slide 23
L15 · PRACTICE SOLUTIONS
Check the rule behind each answer
Textbook: Ch. 6 §§6.1–6.3, pp. 365–380
ELEC 335 | L15 | Week 9
23
Q1
Q⁺=Q⊕T=1⊕1=0.
Q2
Q=1, assuming D has settled. After enable falls, the latch holds 1.
Return to the reference table if your answer used a different rule.
Notes: ELEC 335 | Lecture 15 | Week 9
Practice solutions
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 6 §§6.1–6.3, pp. 365–380.
Companion animation: lesson-01.html
Q1: A T flip-flop has Q=1 and T=1. What is Q⁺?
Q⁺=Q⊕T=1⊕1=0.
Q2: A D latch has enable=1. D changes 0→1 before enable falls. What is Q just before enable falls?
Q=1, assuming D has settled. After enable falls, the latch holds 1.

## Slide 24
L15 · CLOSE
What should stay with you
Textbook: Ch. 6 §§6.1–6.3, pp. 365–380
ELEC 335 | L15 | Week 9
24
Separate present state Q from next state Q⁺
Compare a transparent latch with an edge-triggered flip-flop
Apply D, T, JK and SR characteristic rules
NEXT
Next: Sequential circuit analysis. Use lesson-02.html to preview its model.
Notes: ELEC 335 | Lecture 15 | Week 9
Closing outcomes
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 6 §§6.1–6.3, pp. 365–380.
Companion animation: lesson-01.html
Separate present state Q from next state Q⁺
Compare a transparent latch with an edge-triggered flip-flop
Apply D, T, JK and SR characteristic rules
Next companion: lesson-02.html