## Slide 1
ELEC 335 | Fall 2026
Sequential circuit analysis
Week 9 · Lecture 2
Chapter 6
Digital Logic Design
Textbook: Ch. 6 §6.4, pp. 380–390
Notes: ELEC 335 | Lecture 16 | Week 9
Opening
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 6 §6.4, pp. 380–390.
Companion animation: lesson-02.html
Opening question: How can a circuit be converted into a complete state model?
Outcomes: Derive flip-flop input and next-state equations | Enumerate a state table without missing cases | Distinguish Moore from Mealy output placement

## Slide 2
L16 · READING MAP
Where this lecture sits in the course
Textbook: Ch. 6 §6.4, pp. 380–390
ELEC 335 | L16 | Week 9
2
1
Textbook: Ch. 6 §6.4, pp. 380–390
2
Interactive companion: Lesson 02, Sequential circuit analysis
3
After class: worked examples and practice in the HTML lesson
Preparation: read the named section, then use the worked slides to check each design step.
Notes: ELEC 335 | Lecture 16 | Week 9
Reading map
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 6 §6.4, pp. 380–390.
Companion animation: lesson-02.html

## Slide 3
L16 · LEARNING OUTCOMES
Today's destination
Textbook: Ch. 6 §6.4, pp. 380–390
ELEC 335 | L16 | Week 9
3
01
Derive flip-flop input and next-state equations
02
Enumerate a state table without missing cases
03
Distinguish Moore from Mealy output placement
Course outcome: State tables and diagrams
Notes: ELEC 335 | Lecture 16 | Week 9
Learning outcomes
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 6 §6.4, pp. 380–390.
Companion animation: lesson-02.html
Derive flip-flop input and next-state equations
Enumerate a state table without missing cases
Distinguish Moore from Mealy output placement

## Slide 4
L16 · BIG PICTURE
The question that organizes today
Textbook: Ch. 6 §6.4, pp. 380–390
ELEC 335 | L16 | Week 9
4
How can a circuit be converted into a complete state model?
Keep this question in view as the circuit models and examples develop.
Notes: ELEC 335 | Lecture 16 | Week 9
Guiding question
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 6 §6.4, pp. 380–390.
Companion animation: lesson-02.html
Ask students for an initial answer: How can a circuit be converted into a complete state model?

## Slide 5
L16 · PREREQUISITE BRIDGE
Start from what you already know
Textbook: Ch. 6 §6.4, pp. 380–390
ELEC 335 | L16 | Week 9
5
✓
A gate network can be expressed as Boolean equations.
✓
A flip-flop stores one present-state bit.
✓
A truth table lists every input combination for a fixed state.
Turn to a partner: explain one statement without reading it aloud.
Notes: ELEC 335 | Lecture 16 | Week 9
Prerequisite bridge
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 6 §6.4, pp. 380–390.
Companion animation: lesson-02.html
A gate network can be expressed as Boolean equations.
A flip-flop stores one present-state bit.
A truth table lists every input combination for a fixed state.

## Slide 6
L16 · VOCABULARY
Four words to make precise
Textbook: Ch. 6 §6.4, pp. 380–390
ELEC 335 | L16 | Week 9
6
state equation
Boolean expression for a next-state bit
state table
all present-state and input cases
Moore output
output determined by present state
Mealy output
output determined by state and current input
Use each term when explaining the circuit, table, or timing trace.
Notes: ELEC 335 | Lecture 16 | Week 9
Vocabulary
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 6 §6.4, pp. 380–390.
Companion animation: lesson-02.html
state equation: Boolean expression for a next-state bit
state table: all present-state and input cases
Moore output: output determined by present state
Mealy output: output determined by state and current input

## Slide 7
L16 · PLAIN-LANGUAGE MODEL
The reasoning sequence
Textbook: Ch. 6 §6.4, pp. 380–390
ELEC 335 | L16 | Week 9
7
01
Trace each flip-flop input back through the gates.
02
Apply the flip-flop characteristic equation.
03
Enumerate every state/input row and draw its transition.
How can a circuit be converted into a complete state model?
Notes: ELEC 335 | Lecture 16 | Week 9
Plain-language model
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 6 §6.4, pp. 380–390.
Companion animation: lesson-02.html
Trace each flip-flop input back through the gates.
Apply the flip-flop characteristic equation.
Enumerate every state/input row and draw its transition.

## Slide 8
L16 · REFERENCE
The table to keep beside the method
Textbook: Ch. 6 §6.4, pp. 380–390
ELEC 335 | L16 | Week 9
8
Present Q | Input X | D=X⊕Q | Next Q⁺ | Mealy Z=XQ
0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 1
Name the bit order and control conditions before using a row.
Notes: ELEC 335 | Lecture 16 | Week 9
Reference table
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 6 §6.4, pp. 380–390.
Companion animation: lesson-02.html
Read all columns in the bit order shown. Ask students to predict one row before the worked example.

## Slide 9
L16 · METHOD
A reliable procedure for exercises
Textbook: Ch. 6 §6.4, pp. 380–390
ELEC 335 | L16 | Week 9
9
1
Name every present-state variable and write flip-flop input equations from the gates.
2
Apply the correct characteristic equation to obtain each next-state bit.
3
Enumerate all state/input rows before drawing and checking the diagram.
Complete the table or trace, then verify the circuit one row at a time.
Notes: ELEC 335 | Lecture 16 | Week 9
Textbook exercise method
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 6 §6.4, pp. 380–390.
Companion animation: lesson-02.html
Name every present-state variable and write flip-flop input equations from the gates.
Apply the correct characteristic equation to obtain each next-state bit.
Enumerate all state/input rows before drawing and checking the diagram.

## Slide 10
L16 · WORKED EXAMPLE
Analyze a D flip-flop network
Textbook: Ch. 6 §6.4, pp. 380–390
ELEC 335 | L16 | Week 9
10
One D flip-flop has D=X⊕Q and output Z=XQ. Derive its behavior.
1
Since Q⁺=D, write Q⁺=X⊕Q.
2
For X=0, Q⁺=Q, so both states hold.
3
For X=1, Q⁺=Q′, so both states toggle.
4
Compute Z from the present Q and X for each table row.
Z=1 only on the transition out of Q=1 with X=1. This is a Mealy output.
Notes: ELEC 335 | Lecture 16 | Week 9
Analyze a D flip-flop network
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 6 §6.4, pp. 380–390.
Companion animation: lesson-02.html
Prompt: One D flip-flop has D=X⊕Q and output Z=XQ. Derive its behavior.
Steps:
Since Q⁺=D, write Q⁺=X⊕Q.
For X=0, Q⁺=Q, so both states hold.
For X=1, Q⁺=Q′, so both states toggle.
Compute Z from the present Q and X for each table row.
Answer: Z=1 only on the transition out of Q=1 with X=1. This is a Mealy output.

## Slide 11
L16 · CONCEPT
Two designs to distinguish
Textbook: Ch. 6 §6.4, pp. 380–390
ELEC 335 | L16 | Week 9
11
Moore model
Output belongs inside each state.
Input changes affect output after a state update.
Mealy model
Output belongs on each transition.
Current input can change output within a state.
Explain the difference using behavior and timing, then test one case.
Notes: ELEC 335 | Lecture 16 | Week 9
Concept comparison
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 6 §6.4, pp. 380–390.
Companion animation: lesson-02.html
Moore model | Output belongs inside each state. | Input changes affect output after a state update.
Mealy model | Output belongs on each transition. | Current input can change output within a state.

## Slide 12
L16 · INTERACTIVE COMPANION
From equation to state trace
Textbook: Ch. 6 §6.4, pp. 380–390
ELEC 335 | L16 | Week 9
12
Q=0
→
Q=1
X=1 toggles; X=0 holds
The active row and transition follow D=X⊕Q; Z=XQ responds to the present input and state.
Open lesson-02.html for the animated model and state-by-state controls.
Notes: ELEC 335 | Lecture 16 | Week 9
Interactive model
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 6 §6.4, pp. 380–390.
Companion animation: lesson-02.html
The active row and transition follow D=X⊕Q; Z=XQ responds to the present input and state.
Set X=1 and single-step twice. Trace each active table row aloud.
Ask students to place Z for Q=1, X=1 on a state or on an arrow.
Use the four-row table as the audit of the diagram.

## Slide 13
ACTIVITY
L16
TEAM
TASK
Apply the method together
For D=X⊕Q and Z=XQ, complete all four state/input rows and draw the two-state diagram with output labels.
Name every present-state variable and write flip-flop input equations from the gates.
DELIVERABLE
A complete state table and a diagram with four labelled transitions.
Textbook: Ch. 6 §6.4, pp. 380–390
L16 | Week 9
ELEC 335 | Digital Logic Design
13
Notes: ELEC 335 | Lecture 16 | Week 9
Team activity
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 6 §6.4, pp. 380–390.
Companion animation: lesson-02.html
For D=X⊕Q and Z=XQ, complete all four state/input rows and draw the two-state diagram with output labels.
Deliverable: A complete state table and a diagram with four labelled transitions.

## Slide 14
L16 · GUIDED EXAMPLE
Try the first move before I do
Textbook: Ch. 6 §6.4, pp. 380–390
ELEC 335 | L16 | Week 9
14
A two-state machine holds when X=0 and toggles when X=1. Its Moore output equals the state bit.
YOUR FIRST MOVE
Name the states S0 and S1 with outputs 0 and 1.
Pause for 60–90 seconds. Write, then compare with a partner.
Notes: ELEC 335 | Lecture 16 | Week 9
Guided example
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 6 §6.4, pp. 380–390.
Companion animation: lesson-02.html
Prompt: A two-state machine holds when X=0 and toggles when X=1. Its Moore output equals the state bit.
First move: Name the states S0 and S1 with outputs 0 and 1.
Pause before showing the next slide.

## Slide 15
L16 · GUIDED SOLUTION
Now make every step visible
Textbook: Ch. 6 §6.4, pp. 380–390
ELEC 335 | L16 | Week 9
15
1
Name the states S0 and S1 with outputs 0 and 1.
2
For X=0, draw self-loops on both states.
3
For X=1, draw S0→S1 and S1→S0.
4
Place the output inside each state, not on each arrow.
Four state/input rows are required, one for each pair of state and X.
Notes: ELEC 335 | Lecture 16 | Week 9
Convert a verbal rule to a table
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 6 §6.4, pp. 380–390.
Companion animation: lesson-02.html
Steps:
Name the states S0 and S1 with outputs 0 and 1.
For X=0, draw self-loops on both states.
For X=1, draw S0→S1 and S1→S0.
Place the output inside each state, not on each arrow.
Answer: Four state/input rows are required, one for each pair of state and X.

## Slide 16
L16 · MISCONCEPTION CLINIC
A tempting mistake to remove now
Textbook: Ch. 6 §6.4, pp. 380–390
ELEC 335 | L16 | Week 9
16
TEMPTING CLAIM
An output Z=XQ belongs inside the state node.
WHY IT FAILS
The current input X can change Z before the state changes.
REPAIR
Label Z on the transition for each state/input pair.
Notes: ELEC 335 | Lecture 16 | Week 9
Misconception clinic
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 6 §6.4, pp. 380–390.
Companion animation: lesson-02.html
TEMPTING CLAIM: An output Z=XQ belongs inside the state node.
WHY IT FAILS: The current input X can change Z before the state changes.
REPAIR: Label Z on the transition for each state/input pair.

## Slide 17
L16 · ONE-MINUTE CHECKS
Close the book: can you apply it?
Textbook: Ch. 6 §6.4, pp. 380–390
ELEC 335 | L16 | Week 9
17
Q1
For D=X⊕Q, what transition occurs from Q=1 when X=1?
Q2
A circuit output is Z=QX. Is it Moore or Mealy?
Answer without notes, then compare your reasoning with the next slide.
Notes: ELEC 335 | Lecture 16 | Week 9
Practice questions
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 6 §6.4, pp. 380–390.
Companion animation: lesson-02.html
Q1: For D=X⊕Q, what transition occurs from Q=1 when X=1?
Hint: Compute D first.
Answer: D=1⊕1=0, so Q⁺=0.
Q2: A circuit output is Z=QX. Is it Moore or Mealy?
Hint: Check whether X appears in the output equation.
Answer: Mealy, because the current input X can change Z without a state change.

## Slide 18
L16 · PRACTICE SOLUTIONS
Check the rule behind each answer
Textbook: Ch. 6 §6.4, pp. 380–390
ELEC 335 | L16 | Week 9
18
Q1
D=1⊕1=0, so Q⁺=0.
Q2
Mealy, because the current input X can change Z without a state change.
Return to the reference table if your answer used a different rule.
Notes: ELEC 335 | Lecture 16 | Week 9
Practice solutions
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 6 §6.4, pp. 380–390.
Companion animation: lesson-02.html
Q1: For D=X⊕Q, what transition occurs from Q=1 when X=1?
D=1⊕1=0, so Q⁺=0.
Q2: A circuit output is Z=QX. Is it Moore or Mealy?
Mealy, because the current input X can change Z without a state change.

## Slide 19
L16 · CLOSE
What should stay with you
Textbook: Ch. 6 §6.4, pp. 380–390
ELEC 335 | L16 | Week 9
19
Derive flip-flop input and next-state equations
Enumerate a state table without missing cases
Distinguish Moore from Mealy output placement
NEXT
Next: Flip-flop excitation and synchronous counters. Use lesson-03.html to preview its model.
Notes: ELEC 335 | Lecture 16 | Week 9
Closing outcomes
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 6 §6.4, pp. 380–390.
Companion animation: lesson-02.html
Derive flip-flop input and next-state equations
Enumerate a state table without missing cases
Distinguish Moore from Mealy output placement
Next companion: lesson-03.html