## Slide 1
ELEC 335 | Fall 2026
Flip-flop excitation and synchronous counters
Week 10 · Lecture 1
Chapter 7
Digital Logic Design
Textbook: Ch. 7 §§7.1–7.2, pp. 420–447
Notes: ELEC 335 | Lecture 17 | Week 10
Opening
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §§7.1–7.2, pp. 420–447.
Companion animation: lesson-03.html
Opening question: What input must each flip-flop receive to make a specified transition?
Outcomes: Use D, T and JK excitation requirements | Design a synchronous modulus-six counter | Specify recovery from unused encodings

## Slide 2
L17 · READING MAP
Where this lecture sits in the course
Textbook: Ch. 7 §§7.1–7.2, pp. 420–447
ELEC 335 | L17 | Week 10
2
1
Textbook: Ch. 7 §§7.1–7.2, pp. 420–447
2
Interactive companion: Lesson 03, Flip-flop excitation and synchronous counters
3
After class: worked examples and practice in the HTML lesson
Preparation: read the named section, then use the worked slides to check each design step.
Notes: ELEC 335 | Lecture 17 | Week 10
Reading map
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §§7.1–7.2, pp. 420–447.
Companion animation: lesson-03.html

## Slide 3
L17 · LEARNING OUTCOMES
Today's destination
Textbook: Ch. 7 §§7.1–7.2, pp. 420–447
ELEC 335 | L17 | Week 10
3
01
Use D, T and JK excitation requirements
02
Design a synchronous modulus-six counter
03
Specify recovery from unused encodings
Course outcome: Flip-flop and counter design
Notes: ELEC 335 | Lecture 17 | Week 10
Learning outcomes
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §§7.1–7.2, pp. 420–447.
Companion animation: lesson-03.html
Use D, T and JK excitation requirements
Design a synchronous modulus-six counter
Specify recovery from unused encodings

## Slide 4
L17 · BIG PICTURE
The question that organizes today
Textbook: Ch. 7 §§7.1–7.2, pp. 420–447
ELEC 335 | L17 | Week 10
4
What input must each flip-flop receive to make a specified transition?
Keep this question in view as the circuit models and examples develop.
Notes: ELEC 335 | Lecture 17 | Week 10
Guiding question
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §§7.1–7.2, pp. 420–447.
Companion animation: lesson-03.html
Ask students for an initial answer: What input must each flip-flop receive to make a specified transition?

## Slide 5
L17 · PREREQUISITE BRIDGE
Start from what you already know
Textbook: Ch. 7 §§7.1–7.2, pp. 420–447
ELEC 335 | L17 | Week 10
5
✓
A state table specifies a desired next state.
✓
A D flip-flop copies its input to Q at the edge.
✓
A three-bit register has eight possible binary codes.
Turn to a partner: explain one statement without reading it aloud.
Notes: ELEC 335 | Lecture 17 | Week 10
Prerequisite bridge
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §§7.1–7.2, pp. 420–447.
Companion animation: lesson-03.html
A state table specifies a desired next state.
A D flip-flop copies its input to Q at the edge.
A three-bit register has eight possible binary codes.

## Slide 6
L17 · VOCABULARY
Four words to make precise
Textbook: Ch. 7 §§7.1–7.2, pp. 420–447
ELEC 335 | L17 | Week 10
6
excitation
input required for a specified Q to Q⁺ change
modulus
number of states in a counter cycle
synchronous counter
stages driven by one shared clock
unused encoding
bit pattern outside the intended count sequence
Use each term when explaining the circuit, table, or timing trace.
Notes: ELEC 335 | Lecture 17 | Week 10
Vocabulary
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §§7.1–7.2, pp. 420–447.
Companion animation: lesson-03.html
excitation: input required for a specified Q to Q⁺ change
modulus: number of states in a counter cycle
synchronous counter: stages driven by one shared clock
unused encoding: bit pattern outside the intended count sequence

## Slide 7
L17 · PLAIN-LANGUAGE MODEL
The reasoning sequence
Textbook: Ch. 7 §§7.1–7.2, pp. 420–447
ELEC 335 | L17 | Week 10
7
01
Write the full desired state sequence.
02
Assign every unused encoding a defined recovery.
03
Convert Q to Q⁺ changes into flip-flop inputs and verify.
What input must each flip-flop receive to make a specified transition?
Notes: ELEC 335 | Lecture 17 | Week 10
Plain-language model
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §§7.1–7.2, pp. 420–447.
Companion animation: lesson-03.html
Write the full desired state sequence.
Assign every unused encoding a defined recovery.
Convert Q to Q⁺ changes into flip-flop inputs and verify.

## Slide 8
L17 · REFERENCE
The table to keep beside the method
Textbook: Ch. 7 §§7.1–7.2, pp. 420–447
ELEC 335 | L17 | Week 10
8
Q→Q⁺ | D | T | J | K
0→0 | 0 | 0 | 0 | –
0→1 | 1 | 1 | 1 | –
1→0 | 0 | 1 | – | 1
1→1 | 1 | 0 | – | 0
Name the bit order and control conditions before using a row.
Notes: ELEC 335 | Lecture 17 | Week 10
Reference table
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §§7.1–7.2, pp. 420–447.
Companion animation: lesson-03.html
Read all columns in the bit order shown. Ask students to predict one row before the worked example.

## Slide 9
L17 · METHOD
A reliable procedure for exercises
Textbook: Ch. 7 §§7.1–7.2, pp. 420–447
ELEC 335 | L17 | Week 10
9
1
Write the required state sequence and include every unused encoding.
2
Add excitation columns for the selected flip-flop type.
3
Simplify each input equation and verify every transition by substitution.
Complete the table or trace, then verify the circuit one row at a time.
Notes: ELEC 335 | Lecture 17 | Week 10
Textbook exercise method
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §§7.1–7.2, pp. 420–447.
Companion animation: lesson-03.html
Write the required state sequence and include every unused encoding.
Add excitation columns for the selected flip-flop type.
Simplify each input equation and verify every transition by substitution.

## Slide 10
L17 · WORKED EXAMPLE
Design a mod-6 counter with D flip-flops
Textbook: Ch. 7 §§7.1–7.2, pp. 420–447
ELEC 335 | L17 | Week 10
10
Use Q₂Q₁Q₀ for 000→001→010→011→100→101→000. Send 110 and 111 to 000.
1
List all eight present states, including 110 and 111.
2
For every row, copy each next-state bit to D₂D₁D₀.
3
The ones of D₂ occur at present states 011 and 100.
4
The ones of D₁ occur at 001 and 010. The ones of D₀ occur at 000, 010 and 100.
D₂=Σm(3,4), D₁=Σm(1,2), D₀=Σm(0,2,4), with minterm index Q₂Q₁Q₀.
Notes: ELEC 335 | Lecture 17 | Week 10
Design a mod-6 counter with D flip-flops
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §§7.1–7.2, pp. 420–447.
Companion animation: lesson-03.html
Prompt: Use Q₂Q₁Q₀ for 000→001→010→011→100→101→000. Send 110 and 111 to 000.
Steps:
List all eight present states, including 110 and 111.
For every row, copy each next-state bit to D₂D₁D₀.
The ones of D₂ occur at present states 011 and 100.
The ones of D₁ occur at 001 and 010. The ones of D₀ occur at 000, 010 and 100.
Answer: D₂=Σm(3,4), D₁=Σm(1,2), D₀=Σm(0,2,4), with minterm index Q₂Q₁Q₀.

## Slide 11
L17 · CONCEPT
Two designs to distinguish
Textbook: Ch. 7 §§7.1–7.2, pp. 420–447
ELEC 335 | L17 | Week 10
11
D excitation
Input equals the requested next-state bit.
D=Q⁺.
T excitation
Input requests hold or toggle.
T=Q⊕Q⁺.
Explain the difference using behavior and timing, then test one case.
Notes: ELEC 335 | Lecture 17 | Week 10
Concept comparison
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §§7.1–7.2, pp. 420–447.
Companion animation: lesson-03.html
D excitation | Input equals the requested next-state bit. | D=Q⁺.
T excitation | Input requests hold or toggle. | T=Q⊕Q⁺.

## Slide 12
L17 · INTERACTIVE COMPANION
Mod-6 counter laboratory
Textbook: Ch. 7 §§7.1–7.2, pp. 420–447
ELEC 335 | L17 | Week 10
12
000
→
001
→
010
→
011
→
100
→
101
All stages sample one shared edge
The table assigns 110 and 111 to recover to 000. Watch all three bits update on the same edge.
Open lesson-03.html for the animated model and state-by-state controls.
Notes: ELEC 335 | Lecture 17 | Week 10
Interactive model
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §§7.1–7.2, pp. 420–447.
Companion animation: lesson-03.html
The table assigns 110 and 111 to recover to 000. Watch all three bits update on the same edge.
Start the counter at 101 and ask students to predict the wrap.
Use Set state to inject 110, then clock once to show recovery.
Derive one D input column from the transition table before showing all three equations.

## Slide 13
ACTIVITY
L17
TEAM
TASK
Apply the method together
Build the complete transition table for a mod-6 counter. Assign 110 and 111 to recover to 000, then fill D₂D₁D₀.
Write the required state sequence and include every unused encoding.
DELIVERABLE
Eight present-state rows, next states, and three D-input columns.
Textbook: Ch. 7 §§7.1–7.2, pp. 420–447
L17 | Week 10
ELEC 335 | Digital Logic Design
13
Notes: ELEC 335 | Lecture 17 | Week 10
Team activity
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §§7.1–7.2, pp. 420–447.
Companion animation: lesson-03.html
Build the complete transition table for a mod-6 counter. Assign 110 and 111 to recover to 000, then fill D₂D₁D₀.
Deliverable: Eight present-state rows, next states, and three D-input columns.

## Slide 14
L17 · GUIDED EXAMPLE
Try the first move before I do
Textbook: Ch. 7 §§7.1–7.2, pp. 420–447
ELEC 335 | L17 | Week 10
14
A state bit must move 1→0. Determine D, T and the constrained JK input.
YOUR FIRST MOVE
D must equal the requested next value, so D=0.
Pause for 60–90 seconds. Write, then compare with a partner.
Notes: ELEC 335 | Lecture 17 | Week 10
Guided example
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §§7.1–7.2, pp. 420–447.
Companion animation: lesson-03.html
Prompt: A state bit must move 1→0. Determine D, T and the constrained JK input.
First move: D must equal the requested next value, so D=0.
Pause before showing the next slide.

## Slide 15
L17 · GUIDED SOLUTION
Now make every step visible
Textbook: Ch. 7 §§7.1–7.2, pp. 420–447
ELEC 335 | L17 | Week 10
15
1
D must equal the requested next value, so D=0.
2
T=Q⊕Q⁺=1⊕0=1.
3
For JK, K must be 1; J is a don’t-care because Q=1.
D=0, T=1, J=–, K=1.
Notes: ELEC 335 | Lecture 17 | Week 10
Convert a bit transition into excitation
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §§7.1–7.2, pp. 420–447.
Companion animation: lesson-03.html
Steps:
D must equal the requested next value, so D=0.
T=Q⊕Q⁺=1⊕0=1.
For JK, K must be 1; J is a don’t-care because Q=1.
Answer: D=0, T=1, J=–, K=1.

## Slide 16
L17 · MISCONCEPTION CLINIC
A tempting mistake to remove now
Textbook: Ch. 7 §§7.1–7.2, pp. 420–447
ELEC 335 | L17 | Week 10
16
TEMPTING CLAIM
Unused counter codes can be omitted from the design table.
WHY IT FAILS
A real circuit can enter an unused code after reset, noise, or fault.
REPAIR
Specify recovery and verify every binary code.
Notes: ELEC 335 | Lecture 17 | Week 10
Misconception clinic
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §§7.1–7.2, pp. 420–447.
Companion animation: lesson-03.html
TEMPTING CLAIM: Unused counter codes can be omitted from the design table.
WHY IT FAILS: A real circuit can enter an unused code after reset, noise, or fault.
REPAIR: Specify recovery and verify every binary code.

## Slide 17
L17 · ONE-MINUTE CHECKS
Close the book: can you apply it?
Textbook: Ch. 7 §§7.1–7.2, pp. 420–447
ELEC 335 | L17 | Week 10
17
Q1
A T flip-flop must move 0→0. What T is required?
Q2
How many flip-flops are needed for a mod-10 binary counter?
Answer without notes, then compare your reasoning with the next slide.
Notes: ELEC 335 | Lecture 17 | Week 10
Practice questions
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §§7.1–7.2, pp. 420–447.
Companion animation: lesson-03.html
Q1: A T flip-flop must move 0→0. What T is required?
Hint: Use T=Q⊕Q⁺.
Answer: T=0⊕0=0.
Q2: How many flip-flops are needed for a mod-10 binary counter?
Hint: Find the smallest n for which 2ⁿ≥10.
Answer: Four flip-flops; 2³=8 is insufficient and 2⁴=16 is sufficient.

## Slide 18
L17 · PRACTICE SOLUTIONS
Check the rule behind each answer
Textbook: Ch. 7 §§7.1–7.2, pp. 420–447
ELEC 335 | L17 | Week 10
18
Q1
T=0⊕0=0.
Q2
Four flip-flops; 2³=8 is insufficient and 2⁴=16 is sufficient.
Return to the reference table if your answer used a different rule.
Notes: ELEC 335 | Lecture 17 | Week 10
Practice solutions
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §§7.1–7.2, pp. 420–447.
Companion animation: lesson-03.html
Q1: A T flip-flop must move 0→0. What T is required?
T=0⊕0=0.
Q2: How many flip-flops are needed for a mod-10 binary counter?
Four flip-flops; 2³=8 is insufficient and 2⁴=16 is sufficient.

## Slide 19
L17 · CLOSE
What should stay with you
Textbook: Ch. 7 §§7.1–7.2, pp. 420–447
ELEC 335 | L17 | Week 10
19
Use D, T and JK excitation requirements
Design a synchronous modulus-six counter
Specify recovery from unused encodings
NEXT
Next: Ripple counters and asynchronous behavior. Use lesson-04.html to preview its model.
Notes: ELEC 335 | Lecture 17 | Week 10
Closing outcomes
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §§7.1–7.2, pp. 420–447.
Companion animation: lesson-03.html
Use D, T and JK excitation requirements
Design a synchronous modulus-six counter
Specify recovery from unused encodings
Next companion: lesson-04.html