## Slide 1
ELEC 335 | Fall 2026
Ripple counters and asynchronous behavior
Week 10 · Lecture 2
Chapter 7
Digital Logic Design
Textbook: Ch. 7 §7.3, pp. 447–450; timing extension
Notes: ELEC 335 | Lecture 18 | Week 10
Opening
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §7.3, pp. 447–450; timing extension.
Companion animation: lesson-04.html
Opening question: What changes when state elements do not update on one shared edge?
Outcomes: Trace a ripple counter through transient codes | Explain propagation delay and decode glitches | Recognize a fundamental-mode asynchronous state change

## Slide 2
L18 · READING MAP
Where this lecture sits in the course
Textbook: Ch. 7 §7.3, pp. 447–450; timing extension
ELEC 335 | L18 | Week 10
2
1
Textbook: Ch. 7 §7.3, pp. 447–450; timing extension
2
Interactive companion: Lesson 04, Ripple counters and asynchronous behavior
3
After class: worked examples and practice in the HTML lesson
Preparation: read the named section, then use the worked slides to check each design step.
Notes: ELEC 335 | Lecture 18 | Week 10
Reading map
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §7.3, pp. 447–450; timing extension.
Companion animation: lesson-04.html

## Slide 3
L18 · LEARNING OUTCOMES
Today's destination
Textbook: Ch. 7 §7.3, pp. 447–450; timing extension
ELEC 335 | L18 | Week 10
3
01
Trace a ripple counter through transient codes
02
Explain propagation delay and decode glitches
03
Recognize a fundamental-mode asynchronous state change
Course outcome: Asynchronous sequential circuits and ripple counters
Notes: ELEC 335 | Lecture 18 | Week 10
Learning outcomes
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §7.3, pp. 447–450; timing extension.
Companion animation: lesson-04.html
Trace a ripple counter through transient codes
Explain propagation delay and decode glitches
Recognize a fundamental-mode asynchronous state change

## Slide 4
L18 · BIG PICTURE
The question that organizes today
Textbook: Ch. 7 §7.3, pp. 447–450; timing extension
ELEC 335 | L18 | Week 10
4
What changes when state elements do not update on one shared edge?
Keep this question in view as the circuit models and examples develop.
Notes: ELEC 335 | Lecture 18 | Week 10
Guiding question
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §7.3, pp. 447–450; timing extension.
Companion animation: lesson-04.html
Ask students for an initial answer: What changes when state elements do not update on one shared edge?

## Slide 5
L18 · PREREQUISITE BRIDGE
Start from what you already know
Textbook: Ch. 7 §7.3, pp. 447–450; timing extension
ELEC 335 | L18 | Week 10
5
✓
A synchronous design samples all stages on one clock edge.
✓
A T stage changes state when a triggering edge arrives.
✓
Combinational decoding responds to intermediate signal values.
Turn to a partner: explain one statement without reading it aloud.
Notes: ELEC 335 | Lecture 18 | Week 10
Prerequisite bridge
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §7.3, pp. 447–450; timing extension.
Companion animation: lesson-04.html
A synchronous design samples all stages on one clock edge.
A T stage changes state when a triggering edge arrives.
Combinational decoding responds to intermediate signal values.

## Slide 6
L18 · VOCABULARY
Four words to make precise
Textbook: Ch. 7 §7.3, pp. 447–450; timing extension
ELEC 335 | L18 | Week 10
6
ripple counter
one counter stage clocks the next stage
propagation delay
time between a triggering event and its output response
transient code
temporary bit pattern before settling
fundamental mode
one external input change followed by settling
Use each term when explaining the circuit, table, or timing trace.
Notes: ELEC 335 | Lecture 18 | Week 10
Vocabulary
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §7.3, pp. 447–450; timing extension.
Companion animation: lesson-04.html
ripple counter: one counter stage clocks the next stage
propagation delay: time between a triggering event and its output response
transient code: temporary bit pattern before settling
fundamental mode: one external input change followed by settling

## Slide 7
L18 · PLAIN-LANGUAGE MODEL
The reasoning sequence
Textbook: Ch. 7 §7.3, pp. 447–450; timing extension
ELEC 335 | L18 | Week 10
7
01
State the triggering edge of every stage.
02
Trace the first stage change, then each induced change.
03
Separate transient codes from the final settled count.
What changes when state elements do not update on one shared edge?
Notes: ELEC 335 | Lecture 18 | Week 10
Plain-language model
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §7.3, pp. 447–450; timing extension.
Companion animation: lesson-04.html
State the triggering edge of every stage.
Trace the first stage change, then each induced change.
Separate transient codes from the final settled count.

## Slide 8
L18 · REFERENCE
The table to keep beside the method
Textbook: Ch. 7 §7.3, pp. 447–450; timing extension
ELEC 335 | L18 | Week 10
8
Property | Synchronous counter | Ripple counter
Clocking | Common clock to all stages | One stage clocks the next
Update | Near one edge after logic delay | Cascaded propagation delays
Decode | Stable after settling | May see intermediate codes
Name the bit order and control conditions before using a row.
Notes: ELEC 335 | Lecture 18 | Week 10
Reference table
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §7.3, pp. 447–450; timing extension.
Companion animation: lesson-04.html
Read all columns in the bit order shown. Ask students to predict one row before the worked example.

## Slide 9
L18 · METHOD
A reliable procedure for exercises
Textbook: Ch. 7 §7.3, pp. 447–450; timing extension
ELEC 335 | L18 | Week 10
9
1
State which clock edge triggers each stage and in which bit order.
2
Trace every stage transition and include transient codes before the settled result.
3
For asynchronous feedback, list stable input/state combinations and check the one-input-change assumption.
Complete the table or trace, then verify the circuit one row at a time.
Notes: ELEC 335 | Lecture 18 | Week 10
Textbook exercise method
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §7.3, pp. 447–450; timing extension.
Companion animation: lesson-04.html
State which clock edge triggers each stage and in which bit order.
Trace every stage transition and include transient codes before the settled result.
For asynchronous feedback, list stable input/state combinations and check the one-input-change assumption.

## Slide 10
L18 · WORKED EXAMPLE
Trace 011→100 in a ripple counter
Textbook: Ch. 7 §7.3, pp. 447–450; timing extension
ELEC 335 | L18 | Week 10
10
A three-bit falling-edge toggle chain starts at Q₂Q₁Q₀=011. Show the order after the next external clock event.
1
Q₀ toggles from 1 to 0: 011→010.
2
That falling edge clocks Q₁, which toggles 1→0: 010→000.
3
Q₁ falling clocks Q₂, which toggles 0→1: 000→100.
4
Only 100 is the settled count. 010 and 000 are transient.
The observed path is 011, 010, 000, 100.
Notes: ELEC 335 | Lecture 18 | Week 10
Trace 011→100 in a ripple counter
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §7.3, pp. 447–450; timing extension.
Companion animation: lesson-04.html
Prompt: A three-bit falling-edge toggle chain starts at Q₂Q₁Q₀=011. Show the order after the next external clock event.
Steps:
Q₀ toggles from 1 to 0: 011→010.
That falling edge clocks Q₁, which toggles 1→0: 010→000.
Q₁ falling clocks Q₂, which toggles 0→1: 000→100.
Only 100 is the settled count. 010 and 000 are transient.
Answer: The observed path is 011, 010, 000, 100.

## Slide 11
L18 · CONCEPT
Two designs to distinguish
Textbook: Ch. 7 §7.3, pp. 447–450; timing extension
ELEC 335 | L18 | Week 10
11
Synchronous counter
All stages share the external clock.
State bits update around one edge.
Ripple counter
Each stage clocks the next.
Transitions occur in sequence after delay.
Explain the difference using behavior and timing, then test one case.
Notes: ELEC 335 | Lecture 18 | Week 10
Concept comparison
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §7.3, pp. 447–450; timing extension.
Companion animation: lesson-04.html
Synchronous counter | All stages share the external clock. | State bits update around one edge.
Ripple counter | Each stage clocks the next. | Transitions occur in sequence after delay.

## Slide 12
L18 · INTERACTIVE COMPANION
Propagation-delay microscope
Textbook: Ch. 7 §7.3, pp. 447–450; timing extension
ELEC 335 | L18 | Week 10
12
Q₀
→
Q₁
→
Q₂
011 → 010 → 000 → 100
Step the counter and watch intermediate bit patterns. Slow motion makes the ripple visible.
Open lesson-04.html for the animated model and state-by-state controls.
Notes: ELEC 335 | Lecture 18 | Week 10
Interactive model
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §7.3, pp. 447–450; timing extension.
Companion animation: lesson-04.html
Step the counter and watch intermediate bit patterns. Slow motion makes the ripple visible.
Freeze the 011→100 ripple transition after its first bit change.
Ask the class which transient code a decoder could detect.
Demonstrate that the SR latch responds while the external clock is idle.

## Slide 13
ACTIVITY
L18
TEAM
TASK
Apply the method together
Trace 011 to 100 in a three-stage falling-edge ripple counter. Identify each temporary code a decoder could see.
State which clock edge triggers each stage and in which bit order.
DELIVERABLE
An ordered transition trace and one possible decode hazard.
Textbook: Ch. 7 §7.3, pp. 447–450; timing extension
L18 | Week 10
ELEC 335 | Digital Logic Design
13
Notes: ELEC 335 | Lecture 18 | Week 10
Team activity
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §7.3, pp. 447–450; timing extension.
Companion animation: lesson-04.html
Trace 011 to 100 in a three-stage falling-edge ripple counter. Identify each temporary code a decoder could see.
Deliverable: An ordered transition trace and one possible decode hazard.

## Slide 14
L18 · GUIDED EXAMPLE
Try the first move before I do
Textbook: Ch. 7 §7.3, pp. 447–450; timing extension
ELEC 335 | L18 | Week 10
14
A request S sets an indicator; clear R resets it. The events never assert together. Derive the next-state rule.
YOUR FIRST MOVE
List the stable cases: 00 holds Q, 10 sets Q to 1, and 01 resets Q to 0.
Pause for 60–90 seconds. Write, then compare with a partner.
Notes: ELEC 335 | Lecture 18 | Week 10
Guided example
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §7.3, pp. 447–450; timing extension.
Companion animation: lesson-04.html
Prompt: A request S sets an indicator; clear R resets it. The events never assert together. Derive the next-state rule.
First move: List the stable cases: 00 holds Q, 10 sets Q to 1, and 01 resets Q to 0.
Pause before showing the next slide.

## Slide 15
L18 · GUIDED SOLUTION
Now make every step visible
Textbook: Ch. 7 §7.3, pp. 447–450; timing extension
ELEC 335 | L18 | Week 10
15
1
List the stable cases: 00 holds Q, 10 sets Q to 1, and 01 resets Q to 0.
2
Use a present-state column to cover Q=0 and Q=1 for each permitted input pair.
3
The set term S makes Q⁺=1 whenever S=1. The hold term QR′ preserves Q when R=0.
4
Combine them as Q⁺=S+QR′, valid for the specified mutually exclusive inputs.
An active-high SR latch realizes the rule. Input 11 is outside the specification and must be prevented or resolved by design.
Notes: ELEC 335 | Lecture 18 | Week 10
Design an asynchronous event memory
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §7.3, pp. 447–450; timing extension.
Companion animation: lesson-04.html
Steps:
List the stable cases: 00 holds Q, 10 sets Q to 1, and 01 resets Q to 0.
Use a present-state column to cover Q=0 and Q=1 for each permitted input pair.
The set term S makes Q⁺=1 whenever S=1. The hold term QR′ preserves Q when R=0.
Combine them as Q⁺=S+QR′, valid for the specified mutually exclusive inputs.
Answer: An active-high SR latch realizes the rule. Input 11 is outside the specification and must be prevented or resolved by design.

## Slide 16
L18 · MISCONCEPTION CLINIC
A tempting mistake to remove now
Textbook: Ch. 7 §7.3, pp. 447–450; timing extension
ELEC 335 | L18 | Week 10
16
TEMPTING CLAIM
All ripple-counter bits change at the same instant.
WHY IT FAILS
Each stage waits for the preceding stage’s triggering edge.
REPAIR
Trace every intermediate code in time order.
Notes: ELEC 335 | Lecture 18 | Week 10
Misconception clinic
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §7.3, pp. 447–450; timing extension.
Companion animation: lesson-04.html
TEMPTING CLAIM: All ripple-counter bits change at the same instant.
WHY IT FAILS: Each stage waits for the preceding stage’s triggering edge.
REPAIR: Trace every intermediate code in time order.

## Slide 17
L18 · ONE-MINUTE CHECKS
Close the book: can you apply it?
Textbook: Ch. 7 §7.3, pp. 447–450; timing extension
ELEC 335 | L18 | Week 10
17
Q1
What intermediate codes can appear during ripple transition 001→010?
Q2
Why might a decoder connected to ripple outputs produce a narrow pulse?
Answer without notes, then compare your reasoning with the next slide.
Notes: ELEC 335 | Lecture 18 | Week 10
Practice questions
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §7.3, pp. 447–450; timing extension.
Companion animation: lesson-04.html
Q1: What intermediate codes can appear during ripple transition 001→010?
Hint: Toggle Q₀ first, then react to its falling edge.
Answer: 001→000→010.
Q2: Why might a decoder connected to ripple outputs produce a narrow pulse?
Hint: Consider the intermediate codes before settling.
Answer: Its Boolean condition can become true briefly for a transient state even when the starting and final states do not require that output.

## Slide 18
L18 · PRACTICE SOLUTIONS
Check the rule behind each answer
Textbook: Ch. 7 §7.3, pp. 447–450; timing extension
ELEC 335 | L18 | Week 10
18
Q1
001→000→010.
Q2
Its Boolean condition can become true briefly for a transient state even when the starting and final states do not require that output.
Return to the reference table if your answer used a different rule.
Notes: ELEC 335 | Lecture 18 | Week 10
Practice solutions
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §7.3, pp. 447–450; timing extension.
Companion animation: lesson-04.html
Q1: What intermediate codes can appear during ripple transition 001→010?
001→000→010.
Q2: Why might a decoder connected to ripple outputs produce a narrow pulse?
Its Boolean condition can become true briefly for a transient state even when the starting and final states do not require that output.

## Slide 19
L18 · CLOSE
What should stay with you
Textbook: Ch. 7 §7.3, pp. 447–450; timing extension
ELEC 335 | L18 | Week 10
19
Trace a ripple counter through transient codes
Explain propagation delay and decode glitches
Recognize a fundamental-mode asynchronous state change
NEXT
Next: Registers and counter families. Use lesson-05.html to preview its model.
Notes: ELEC 335 | Lecture 18 | Week 10
Closing outcomes
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §7.3, pp. 447–450; timing extension.
Companion animation: lesson-04.html
Trace a ripple counter through transient codes
Explain propagation delay and decode glitches
Recognize a fundamental-mode asynchronous state change
Next companion: lesson-05.html