## Slide 1
ELEC 335 | Fall 2026
Registers and counter families
Week 11 · Lecture 1
Chapter 8
Digital Logic Design
Textbook: Ch. 8 §§8.1–8.2, pp. 493–506
Notes: ELEC 335 | Lecture 19 | Week 11
Opening
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 8 §§8.1–8.2, pp. 493–506.
Companion animation: lesson-05.html
Opening question: How do storage arrangements trade pins, clock cycles and decoding effort?
Outcomes: Trace SISO, SIPO, PISO and PIPO transfers | Determine shift-register latency | Trace ring and Johnson counter cycles

## Slide 2
L19 · READING MAP
Where this lecture sits in the course
Textbook: Ch. 8 §§8.1–8.2, pp. 493–506
ELEC 335 | L19 | Week 11
2
1
Textbook: Ch. 8 §§8.1–8.2, pp. 493–506
2
Interactive companion: Lesson 05, Registers and counter families
3
After class: worked examples and practice in the HTML lesson
Preparation: read the named section, then use the worked slides to check each design step.
Notes: ELEC 335 | Lecture 19 | Week 11
Reading map
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 8 §§8.1–8.2, pp. 493–506.
Companion animation: lesson-05.html

## Slide 3
L19 · LEARNING OUTCOMES
Today's destination
Textbook: Ch. 8 §§8.1–8.2, pp. 493–506
ELEC 335 | L19 | Week 11
3
01
Trace SISO, SIPO, PISO and PIPO transfers
02
Determine shift-register latency
03
Trace ring and Johnson counter cycles
Course outcome: Serial, parallel, shift registers and counters
Notes: ELEC 335 | Lecture 19 | Week 11
Learning outcomes
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 8 §§8.1–8.2, pp. 493–506.
Companion animation: lesson-05.html
Trace SISO, SIPO, PISO and PIPO transfers
Determine shift-register latency
Trace ring and Johnson counter cycles

## Slide 4
L19 · BIG PICTURE
The question that organizes today
Textbook: Ch. 8 §§8.1–8.2, pp. 493–506
ELEC 335 | L19 | Week 11
4
How do storage arrangements trade pins, clock cycles and decoding effort?
Keep this question in view as the circuit models and examples develop.
Notes: ELEC 335 | Lecture 19 | Week 11
Guiding question
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 8 §§8.1–8.2, pp. 493–506.
Companion animation: lesson-05.html
Ask students for an initial answer: How do storage arrangements trade pins, clock cycles and decoding effort?

## Slide 5
L19 · PREREQUISITE BRIDGE
Start from what you already know
Textbook: Ch. 8 §§8.1–8.2, pp. 493–506
ELEC 335 | L19 | Week 11
5
✓
One flip-flop stores one bit.
✓
Several stages can update on the same edge.
✓
A feedback connection can turn a register into a counter.
Turn to a partner: explain one statement without reading it aloud.
Notes: ELEC 335 | Lecture 19 | Week 11
Prerequisite bridge
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 8 §§8.1–8.2, pp. 493–506.
Companion animation: lesson-05.html
One flip-flop stores one bit.
Several stages can update on the same edge.
A feedback connection can turn a register into a counter.

## Slide 6
L19 · VOCABULARY
Four words to make precise
Textbook: Ch. 8 §§8.1–8.2, pp. 493–506
ELEC 335 | L19 | Week 11
6
SISO
serial input and serial output
SIPO
serial input and parallel output
PISO
parallel input and serial output
Johnson counter
shift register fed by the inverse end bit
Use each term when explaining the circuit, table, or timing trace.
Notes: ELEC 335 | Lecture 19 | Week 11
Vocabulary
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 8 §§8.1–8.2, pp. 493–506.
Companion animation: lesson-05.html
SISO: serial input and serial output
SIPO: serial input and parallel output
PISO: parallel input and serial output
Johnson counter: shift register fed by the inverse end bit

## Slide 7
L19 · PLAIN-LANGUAGE MODEL
The reasoning sequence
Textbook: Ch. 8 §§8.1–8.2, pp. 493–506
ELEC 335 | L19 | Week 11
7
01
Label the stage order and shift direction.
02
Write the whole word after each active edge.
03
Count unique states until a feedback cycle returns to reset.
How do storage arrangements trade pins, clock cycles and decoding effort?
Notes: ELEC 335 | Lecture 19 | Week 11
Plain-language model
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 8 §§8.1–8.2, pp. 493–506.
Companion animation: lesson-05.html
Label the stage order and shift direction.
Write the whole word after each active edge.
Count unique states until a feedback cycle returns to reset.

## Slide 8
L19 · REFERENCE
The table to keep beside the method
Textbook: Ch. 8 §§8.1–8.2, pp. 493–506
ELEC 335 | L19 | Week 11
8
Mode | Input | Output | Typical purpose
SISO | Serial | Serial | Delay line
SIPO | Serial | Parallel | Receive a word
PISO | Parallel | Serial | Transmit a word
PIPO | Parallel | Parallel | Store a word
Name the bit order and control conditions before using a row.
Notes: ELEC 335 | Lecture 19 | Week 11
Reference table
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 8 §§8.1–8.2, pp. 493–506.
Companion animation: lesson-05.html
Read all columns in the bit order shown. Ask students to predict one row before the worked example.

## Slide 9
L19 · METHOD
A reliable procedure for exercises
Textbook: Ch. 8 §§8.1–8.2, pp. 493–506
ELEC 335 | L19 | Week 11
9
1
Mark bit order, shift direction, and whether load is serial or parallel.
2
Write the entire register word after each active edge.
3
For feedback counters, continue until the initial word returns and count unique states.
Complete the table or trace, then verify the circuit one row at a time.
Notes: ELEC 335 | Lecture 19 | Week 11
Textbook exercise method
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 8 §§8.1–8.2, pp. 493–506.
Companion animation: lesson-05.html
Mark bit order, shift direction, and whether load is serial or parallel.
Write the entire register word after each active edge.
For feedback counters, continue until the initial word returns and count unique states.

## Slide 10
L19 · WORKED EXAMPLE
Fill a SIPO register
Textbook: Ch. 8 §§8.1–8.2, pp. 493–506
ELEC 335 | L19 | Week 11
10
A four-stage register begins 0000. Enter serial bits 1,0,1,1 at the left end on four edges.
1
After 1: 1000.
2
After 0: 0100.
3
After 1: 1010.
4
After 1: 1101.
The parallel word is 1101 after four edges.
Notes: ELEC 335 | Lecture 19 | Week 11
Fill a SIPO register
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 8 §§8.1–8.2, pp. 493–506.
Companion animation: lesson-05.html
Prompt: A four-stage register begins 0000. Enter serial bits 1,0,1,1 at the left end on four edges.
Steps:
After 1: 1000.
After 0: 0100.
After 1: 1010.
After 1: 1101.
Answer: The parallel word is 1101 after four edges.

## Slide 11
L19 · CONCEPT
Two designs to distinguish
Textbook: Ch. 8 §§8.1–8.2, pp. 493–506
ELEC 335 | L19 | Week 11
11
Ring counter
Recirculates one asserted bit.
N intended states for N stages.
Johnson counter
Feeds back the complement of the end bit.
2N intended states from reset.
Explain the difference using behavior and timing, then test one case.
Notes: ELEC 335 | Lecture 19 | Week 11
Concept comparison
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 8 §§8.1–8.2, pp. 493–506.
Companion animation: lesson-05.html
Ring counter | Recirculates one asserted bit. | N intended states for N stages.
Johnson counter | Feeds back the complement of the end bit. | 2N intended states from reset.

## Slide 12
L19 · INTERACTIVE COMPANION
Four-stage register
Textbook: Ch. 8 §§8.1–8.2, pp. 493–506
ELEC 335 | L19 | Week 11
12
Q₃
→
Q₂
→
Q₁
→
Q₀
One shift on each active edge
Select a transfer mode, load a word or enter serial bits, and advance one edge at a time.
Open lesson-05.html for the animated model and state-by-state controls.
Notes: ELEC 335 | Lecture 19 | Week 11
Interactive model
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 8 §§8.1–8.2, pp. 493–506.
Companion animation: lesson-05.html
Select a transfer mode, load a word or enter serial bits, and advance one edge at a time.
Load 1011 in PISO mode and ask for the output sequence before clocking.
Toggle between ring and Johnson modes and count states to reset.
Have students distinguish a bit’s entry latency from the full word’s fill latency.

## Slide 13
ACTIVITY
L19
TEAM
TASK
Apply the method together
Start a four-stage register at 0000. Shift in 1,0,1,1 at the left. Record the word after every edge and identify the SIPO output.
Mark bit order, shift direction, and whether load is serial or parallel.
DELIVERABLE
Four edge-by-edge register words and the final parallel output.
Textbook: Ch. 8 §§8.1–8.2, pp. 493–506
L19 | Week 11
ELEC 335 | Digital Logic Design
13
Notes: ELEC 335 | Lecture 19 | Week 11
Team activity
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 8 §§8.1–8.2, pp. 493–506.
Companion animation: lesson-05.html
Start a four-stage register at 0000. Shift in 1,0,1,1 at the left. Record the word after every edge and identify the SIPO output.
Deliverable: Four edge-by-edge register words and the final parallel output.

## Slide 14
L19 · GUIDED EXAMPLE
Try the first move before I do
Textbook: Ch. 8 §§8.1–8.2, pp. 493–506
ELEC 335 | L19 | Week 11
14
Starting at 0000, shift right and insert the inverse of the rightmost bit.
YOUR FIRST MOVE
First four edges: 1000, 1100, 1110, 1111.
Pause for 60–90 seconds. Write, then compare with a partner.
Notes: ELEC 335 | Lecture 19 | Week 11
Guided example
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 8 §§8.1–8.2, pp. 493–506.
Companion animation: lesson-05.html
Prompt: Starting at 0000, shift right and insert the inverse of the rightmost bit.
First move: First four edges: 1000, 1100, 1110, 1111.
Pause before showing the next slide.

## Slide 15
L19 · GUIDED SOLUTION
Now make every step visible
Textbook: Ch. 8 §§8.1–8.2, pp. 493–506
ELEC 335 | L19 | Week 11
15
1
First four edges: 1000, 1100, 1110, 1111.
2
Now the rightmost bit is 1, so zeros enter.
3
Next states: 0111, 0011, 0001, 0000.
The cycle has eight states, equal to 2N for N=4.
Notes: ELEC 335 | Lecture 19 | Week 11
Trace a four-stage Johnson counter
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 8 §§8.1–8.2, pp. 493–506.
Companion animation: lesson-05.html
Steps:
First four edges: 1000, 1100, 1110, 1111.
Now the rightmost bit is 1, so zeros enter.
Next states: 0111, 0011, 0001, 0000.
Answer: The cycle has eight states, equal to 2N for N=4.

## Slide 16
L19 · MISCONCEPTION CLINIC
A tempting mistake to remove now
Textbook: Ch. 8 §§8.1–8.2, pp. 493–506
ELEC 335 | L19 | Week 11
16
TEMPTING CLAIM
Four serial bits enter a four-stage register in one edge.
WHY IT FAILS
Serial input accepts one new bit at each edge.
REPAIR
Write the full register word after every edge.
Notes: ELEC 335 | Lecture 19 | Week 11
Misconception clinic
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 8 §§8.1–8.2, pp. 493–506.
Companion animation: lesson-05.html
TEMPTING CLAIM: Four serial bits enter a four-stage register in one edge.
WHY IT FAILS: Serial input accepts one new bit at each edge.
REPAIR: Write the full register word after every edge.

## Slide 17
L19 · ONE-MINUTE CHECKS
Close the book: can you apply it?
Textbook: Ch. 8 §§8.1–8.2, pp. 493–506
ELEC 335 | L19 | Week 11
17
Q1
How many intended states has a five-stage one-hot ring counter?
Q2
A loaded four-bit PISO register emits its rightmost bit first. What serial sequence comes from 1011?
Answer without notes, then compare your reasoning with the next slide.
Notes: ELEC 335 | Lecture 19 | Week 11
Practice questions
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 8 §§8.1–8.2, pp. 493–506.
Companion animation: lesson-05.html
Q1: How many intended states has a five-stage one-hot ring counter?
Hint: The single 1 occupies each stage once.
Answer: Five.
Q2: A loaded four-bit PISO register emits its rightmost bit first. What serial sequence comes from 1011?
Hint: Read rightmost bit, then shift right each edge.
Answer: 1, 1, 0, 1.

## Slide 18
L19 · PRACTICE SOLUTIONS
Check the rule behind each answer
Textbook: Ch. 8 §§8.1–8.2, pp. 493–506
ELEC 335 | L19 | Week 11
18
Q1
Five.
Q2
1, 1, 0, 1.
Return to the reference table if your answer used a different rule.
Notes: ELEC 335 | Lecture 19 | Week 11
Practice solutions
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 8 §§8.1–8.2, pp. 493–506.
Companion animation: lesson-05.html
Q1: How many intended states has a five-stage one-hot ring counter?
Five.
Q2: A loaded four-bit PISO register emits its rightmost bit first. What serial sequence comes from 1011?
1, 1, 0, 1.

## Slide 19
L19 · CLOSE
What should stay with you
Textbook: Ch. 8 §§8.1–8.2, pp. 493–506
ELEC 335 | L19 | Week 11
19
Trace SISO, SIPO, PISO and PIPO transfers
Determine shift-register latency
Trace ring and Johnson counter cycles
NEXT
Next: FSM synthesis, ASM and encoding. Use lesson-06.html to preview its model.
Notes: ELEC 335 | Lecture 19 | Week 11
Closing outcomes
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 8 §§8.1–8.2, pp. 493–506.
Companion animation: lesson-05.html
Trace SISO, SIPO, PISO and PIPO transfers
Determine shift-register latency
Trace ring and Johnson counter cycles
Next companion: lesson-06.html