## Slide 1
ELEC 335 | Fall 2026
FSM synthesis, ASM and encoding
Week 11 · Lecture 2
Chapters 7 and 8
Digital Logic Design
Textbook: Ch. 7 §7.4, pp. 450–465; Ch. 8 §§8.4–8.6, pp. 511–518
Notes: ELEC 335 | Lecture 20 | Week 11
Opening
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §7.4, pp. 450–465; Ch. 8 §§8.4–8.6, pp. 511–518.
Companion animation: lesson-06.html
Opening question: What history must a detector remember to report an overlapping pattern?
Outcomes: Derive states from useful input suffixes | Design an overlapping 101 detector | Interpret an ASM block and compare binary with one-hot encoding

## Slide 2
L20 · READING MAP
Where this lecture sits in the course
Textbook: Ch. 7 §7.4, pp. 450–465; Ch. 8 §§8.4–8.6, pp. 511–518
ELEC 335 | L20 | Week 11
2
1
Textbook: Ch. 7 §7.4, pp. 450–465; Ch. 8 §§8.4–8.6, pp. 511–518
2
Interactive companion: Lesson 06, FSM synthesis, ASM and encoding
3
After class: worked examples and practice in the HTML lesson
Preparation: read the named section, then use the worked slides to check each design step.
Notes: ELEC 335 | Lecture 20 | Week 11
Reading map
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §7.4, pp. 450–465; Ch. 8 §§8.4–8.6, pp. 511–518.
Companion animation: lesson-06.html

## Slide 3
L20 · LEARNING OUTCOMES
Today's destination
Textbook: Ch. 7 §7.4, pp. 450–465; Ch. 8 §§8.4–8.6, pp. 511–518
ELEC 335 | L20 | Week 11
3
01
Derive states from useful input suffixes
02
Design an overlapping 101 detector
03
Interpret an ASM block and compare binary with one-hot encoding
Course outcome: State diagrams and sequential design
Notes: ELEC 335 | Lecture 20 | Week 11
Learning outcomes
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §7.4, pp. 450–465; Ch. 8 §§8.4–8.6, pp. 511–518.
Companion animation: lesson-06.html
Derive states from useful input suffixes
Design an overlapping 101 detector
Interpret an ASM block and compare binary with one-hot encoding

## Slide 4
L20 · BIG PICTURE
The question that organizes today
Textbook: Ch. 7 §7.4, pp. 450–465; Ch. 8 §§8.4–8.6, pp. 511–518
ELEC 335 | L20 | Week 11
4
What history must a detector remember to report an overlapping pattern?
Keep this question in view as the circuit models and examples develop.
Notes: ELEC 335 | Lecture 20 | Week 11
Guiding question
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §7.4, pp. 450–465; Ch. 8 §§8.4–8.6, pp. 511–518.
Companion animation: lesson-06.html
Ask students for an initial answer: What history must a detector remember to report an overlapping pattern?

## Slide 5
L20 · PREREQUISITE BRIDGE
Start from what you already know
Textbook: Ch. 7 §7.4, pp. 450–465; Ch. 8 §§8.4–8.6, pp. 511–518
ELEC 335 | L20 | Week 11
5
✓
A state represents the history needed for future behavior.
✓
A Mealy output may be attached to an input-labelled transition.
✓
Binary codes are assigned after state meanings are settled.
Turn to a partner: explain one statement without reading it aloud.
Notes: ELEC 335 | Lecture 20 | Week 11
Prerequisite bridge
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §7.4, pp. 450–465; Ch. 8 §§8.4–8.6, pp. 511–518.
Companion animation: lesson-06.html
A state represents the history needed for future behavior.
A Mealy output may be attached to an input-labelled transition.
Binary codes are assigned after state meanings are settled.

## Slide 6
L20 · VOCABULARY
Four words to make precise
Textbook: Ch. 7 §7.4, pp. 450–465; Ch. 8 §§8.4–8.6, pp. 511–518
ELEC 335 | L20 | Week 11
6
useful suffix
recent input ending that could begin a target pattern
overlap
one detection shares bits with the next
ASM block
chart element for state actions or decisions
one-hot encoding
one state bit asserted per valid state
Use each term when explaining the circuit, table, or timing trace.
Notes: ELEC 335 | Lecture 20 | Week 11
Vocabulary
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §7.4, pp. 450–465; Ch. 8 §§8.4–8.6, pp. 511–518.
Companion animation: lesson-06.html
useful suffix: recent input ending that could begin a target pattern
overlap: one detection shares bits with the next
ASM block: chart element for state actions or decisions
one-hot encoding: one state bit asserted per valid state

## Slide 7
L20 · PLAIN-LANGUAGE MODEL
The reasoning sequence
Textbook: Ch. 7 §7.4, pp. 450–465; Ch. 8 §§8.4–8.6, pp. 511–518
ELEC 335 | L20 | Week 11
7
01
Name each useful suffix as a state.
02
Append each input and keep the longest useful suffix.
03
Place detection on the completing transition and choose codes.
What history must a detector remember to report an overlapping pattern?
Notes: ELEC 335 | Lecture 20 | Week 11
Plain-language model
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §7.4, pp. 450–465; Ch. 8 §§8.4–8.6, pp. 511–518.
Companion animation: lesson-06.html
Name each useful suffix as a state.
Append each input and keep the longest useful suffix.
Place detection on the completing transition and choose codes.

## Slide 8
L20 · REFERENCE
The table to keep beside the method
Textbook: Ch. 7 §7.4, pp. 450–465; Ch. 8 §§8.4–8.6, pp. 511–518
ELEC 335 | L20 | Week 11
8
Present state | X=0: next/Z | X=1: next/Z
S₀ (none) | S₀ / 0 | S₁ / 0
S₁ (1) | S₂ / 0 | S₁ / 0
S₂ (10) | S₀ / 0 | S₁ / 1
Name the bit order and control conditions before using a row.
Notes: ELEC 335 | Lecture 20 | Week 11
Reference table
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §7.4, pp. 450–465; Ch. 8 §§8.4–8.6, pp. 511–518.
Companion animation: lesson-06.html
Read all columns in the bit order shown. Ask students to predict one row before the worked example.

## Slide 9
L20 · METHOD
A reliable procedure for exercises
Textbook: Ch. 7 §7.4, pp. 450–465; Ch. 8 §§8.4–8.6, pp. 511–518
ELEC 335 | L20 | Week 11
9
1
Identify the shortest history that affects future output and name one state per useful history.
2
For every state and input, append the bit, place any output, and retain the longest useful suffix.
3
Only after the diagram is complete, assign codes and derive next-state equations.
Complete the table or trace, then verify the circuit one row at a time.
Notes: ELEC 335 | Lecture 20 | Week 11
Textbook exercise method
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §7.4, pp. 450–465; Ch. 8 §§8.4–8.6, pp. 511–518.
Companion animation: lesson-06.html
Identify the shortest history that affects future output and name one state per useful history.
For every state and input, append the bit, place any output, and retain the longest useful suffix.
Only after the diagram is complete, assign codes and derive next-state equations.

## Slide 10
L20 · WORKED EXAMPLE
Derive the 101 state table
Textbook: Ch. 7 §7.4, pp. 450–465; Ch. 8 §§8.4–8.6, pp. 511–518
ELEC 335 | L20 | Week 11
10
Detect every overlapping occurrence of 101 in a serial stream.
1
S₀ stores no useful suffix. Input 1 moves to S₁.
2
S₁ stores suffix 1. Input 0 moves to S₂; input 1 stays S₁.
3
S₂ stores suffix 10. Input 1 asserts Z=1 and moves to S₁.
4
Input 0 from S₂ gives 100, with no useful suffix, so return to S₀.
The Mealy machine has three states and detects both occurrences in 10101.
Notes: ELEC 335 | Lecture 20 | Week 11
Derive the 101 state table
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §7.4, pp. 450–465; Ch. 8 §§8.4–8.6, pp. 511–518.
Companion animation: lesson-06.html
Prompt: Detect every overlapping occurrence of 101 in a serial stream.
Steps:
S₀ stores no useful suffix. Input 1 moves to S₁.
S₁ stores suffix 1. Input 0 moves to S₂; input 1 stays S₁.
S₂ stores suffix 10. Input 1 asserts Z=1 and moves to S₁.
Input 0 from S₂ gives 100, with no useful suffix, so return to S₀.
Answer: The Mealy machine has three states and detects both occurrences in 10101.

## Slide 11
L20 · CONCEPT
Two designs to distinguish
Textbook: Ch. 7 §7.4, pp. 450–465; Ch. 8 §§8.4–8.6, pp. 511–518
ELEC 335 | L20 | Week 11
11
Binary encoding
Needs ⌈log₂N⌉ flip-flops for N states.
May require more state decoding.
One-hot encoding
Needs N flip-flops for N states.
Can simplify some next-state logic.
Explain the difference using behavior and timing, then test one case.
Notes: ELEC 335 | Lecture 20 | Week 11
Concept comparison
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §7.4, pp. 450–465; Ch. 8 §§8.4–8.6, pp. 511–518.
Companion animation: lesson-06.html
Binary encoding | Needs ⌈log₂N⌉ flip-flops for N states. | May require more state decoding.
One-hot encoding | Needs N flip-flops for N states. | Can simplify some next-state logic.

## Slide 12
L20 · INTERACTIVE COMPANION
Overlapping 101 detector
Textbook: Ch. 7 §7.4, pp. 450–465; Ch. 8 §§8.4–8.6, pp. 511–518
ELEC 335 | L20 | Week 11
12
S₀: none
→
S₁: 1
→
S₂: 10
S₂ + 1 detects 101 and returns to S₁
Enter bits one by one or play 10101. Watch the retained suffix and the detection pulse.
Open lesson-06.html for the animated model and state-by-state controls.
Notes: ELEC 335 | Lecture 20 | Week 11
Interactive model
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §7.4, pp. 450–465; Ch. 8 §§8.4–8.6, pp. 511–518.
Companion animation: lesson-06.html
Enter bits one by one or play 10101. Watch the retained suffix and the detection pulse.
Enter 10101 and pause at the first detection. Ask why the next state is S₁.
Draw the three suffix meanings before showing codes.
Translate one transition into an ASM decision path.

## Slide 13
ACTIVITY
L20
TEAM
TASK
Apply the method together
Feed 10101 to an overlapping 101 detector. Mark the state after every bit and the two detection pulses.
Identify the shortest history that affects future output and name one state per useful history.
DELIVERABLE
A five-step state trace with each output pulse identified.
Textbook: Ch. 7 §7.4, pp. 450–465; Ch. 8 §§8.4–8.6, pp. 511–518
L20 | Week 11
ELEC 335 | Digital Logic Design
13
Notes: ELEC 335 | Lecture 20 | Week 11
Team activity
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §7.4, pp. 450–465; Ch. 8 §§8.4–8.6, pp. 511–518.
Companion animation: lesson-06.html
Feed 10101 to an overlapping 101 detector. Mark the state after every bit and the two detection pulses.
Deliverable: A five-step state trace with each output pulse identified.

## Slide 14
L20 · GUIDED EXAMPLE
Try the first move before I do
Textbook: Ch. 7 §7.4, pp. 450–465; Ch. 8 §§8.4–8.6, pp. 511–518
ELEC 335 | L20 | Week 11
14
Encode a five-state controller with binary and one-hot assignments.
YOUR FIRST MOVE
Binary needs ⌈log₂5⌉=3 flip-flops.
Pause for 60–90 seconds. Write, then compare with a partner.
Notes: ELEC 335 | Lecture 20 | Week 11
Guided example
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §7.4, pp. 450–465; Ch. 8 §§8.4–8.6, pp. 511–518.
Companion animation: lesson-06.html
Prompt: Encode a five-state controller with binary and one-hot assignments.
First move: Binary needs ⌈log₂5⌉=3 flip-flops.
Pause before showing the next slide.

## Slide 15
L20 · GUIDED SOLUTION
Now make every step visible
Textbook: Ch. 7 §7.4, pp. 450–465; Ch. 8 §§8.4–8.6, pp. 511–518
ELEC 335 | L20 | Week 11
15
1
Binary needs ⌈log₂5⌉=3 flip-flops.
2
One-hot needs five flip-flops.
3
Binary leaves three unused codes; one-hot leaves many invalid patterns.
4
Compare next-state logic, reset strategy and timing before choosing.
Storage counts are 3 versus 5; neither count alone determines the best implementation.
Notes: ELEC 335 | Lecture 20 | Week 11
Choose an encoding
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §7.4, pp. 450–465; Ch. 8 §§8.4–8.6, pp. 511–518.
Companion animation: lesson-06.html
Steps:
Binary needs ⌈log₂5⌉=3 flip-flops.
One-hot needs five flip-flops.
Binary leaves three unused codes; one-hot leaves many invalid patterns.
Compare next-state logic, reset strategy and timing before choosing.
Answer: Storage counts are 3 versus 5; neither count alone determines the best implementation.

## Slide 16
L20 · MISCONCEPTION CLINIC
A tempting mistake to remove now
Textbook: Ch. 7 §7.4, pp. 450–465; Ch. 8 §§8.4–8.6, pp. 511–518
ELEC 335 | L20 | Week 11
16
TEMPTING CLAIM
After detecting 101, the machine returns to the empty-suffix state.
WHY IT FAILS
The last 1 is already a useful prefix of the next occurrence.
REPAIR
Return to the suffix-1 state to allow overlap.
Notes: ELEC 335 | Lecture 20 | Week 11
Misconception clinic
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §7.4, pp. 450–465; Ch. 8 §§8.4–8.6, pp. 511–518.
Companion animation: lesson-06.html
TEMPTING CLAIM: After detecting 101, the machine returns to the empty-suffix state.
WHY IT FAILS: The last 1 is already a useful prefix of the next occurrence.
REPAIR: Return to the suffix-1 state to allow overlap.

## Slide 17
L20 · ONE-MINUTE CHECKS
Close the book: can you apply it?
Textbook: Ch. 7 §7.4, pp. 450–465; Ch. 8 §§8.4–8.6, pp. 511–518
ELEC 335 | L20 | Week 11
17
Q1
What state follows S₂ after input 1 in the overlapping 101 detector?
Q2
How many state bits does binary encoding need for 12 states?
Answer without notes, then compare your reasoning with the next slide.
Notes: ELEC 335 | Lecture 20 | Week 11
Practice questions
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §7.4, pp. 450–465; Ch. 8 §§8.4–8.6, pp. 511–518.
Companion animation: lesson-06.html
Q1: What state follows S₂ after input 1 in the overlapping 101 detector?
Hint: The final 1 is a useful prefix.
Answer: S₁, with Z=1 on that transition.
Q2: How many state bits does binary encoding need for 12 states?
Hint: Find the smallest n with 2ⁿ≥12.
Answer: Four bits.

## Slide 18
L20 · PRACTICE SOLUTIONS
Check the rule behind each answer
Textbook: Ch. 7 §7.4, pp. 450–465; Ch. 8 §§8.4–8.6, pp. 511–518
ELEC 335 | L20 | Week 11
18
Q1
S₁, with Z=1 on that transition.
Q2
Four bits.
Return to the reference table if your answer used a different rule.
Notes: ELEC 335 | Lecture 20 | Week 11
Practice solutions
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §7.4, pp. 450–465; Ch. 8 §§8.4–8.6, pp. 511–518.
Companion animation: lesson-06.html
Q1: What state follows S₂ after input 1 in the overlapping 101 detector?
S₁, with Z=1 on that transition.
Q2: How many state bits does binary encoding need for 12 states?
Four bits.

## Slide 19
L20 · CLOSE
What should stay with you
Textbook: Ch. 7 §7.4, pp. 450–465; Ch. 8 §§8.4–8.6, pp. 511–518
ELEC 335 | L20 | Week 11
19
Derive states from useful input suffixes
Design an overlapping 101 detector
Interpret an ASM block and compare binary with one-hot encoding
NEXT
Next: ROM, PLA and PAL implementation. Use lesson-07.html to preview its model.
Notes: ELEC 335 | Lecture 20 | Week 11
Closing outcomes
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 7 §7.4, pp. 450–465; Ch. 8 §§8.4–8.6, pp. 511–518.
Companion animation: lesson-06.html
Derive states from useful input suffixes
Design an overlapping 101 detector
Interpret an ASM block and compare binary with one-hot encoding
Next companion: lesson-07.html