## Slide 1
ELEC 335 | Fall 2026
ROM, PLA and PAL implementation
Week 12 · Lecture 1
Chapters 5 and 8
Digital Logic Design
Textbook: Ch. 5 §5.6, pp. 276 onward; Ch. 8 §8.3, pp. 506–511
Notes: ELEC 335 | Lecture 21 | Week 12
Opening
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 5 §5.6, pp. 276 onward; Ch. 8 §8.3, pp. 506–511.
Companion animation: lesson-07.html
Opening question: How can one truth table be realized with three programmable structures?
Outcomes: Map inputs to ROM addresses and output words | Build shared product terms in a PLA | Explain fixed OR allocation in a PAL

## Slide 2
L21 · READING MAP
Where this lecture sits in the course
Textbook: Ch. 5 §5.6, pp. 276 onward; Ch. 8 §8.3, pp. 506–511
ELEC 335 | L21 | Week 12
2
1
Textbook: Ch. 5 §5.6, pp. 276 onward; Ch. 8 §8.3, pp. 506–511
2
Interactive companion: Lesson 07, ROM, PLA and PAL implementation
3
After class: worked examples and practice in the HTML lesson
Preparation: read the named section, then use the worked slides to check each design step.
Notes: ELEC 335 | Lecture 21 | Week 12
Reading map
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 5 §5.6, pp. 276 onward; Ch. 8 §8.3, pp. 506–511.
Companion animation: lesson-07.html

## Slide 3
L21 · LEARNING OUTCOMES
Today's destination
Textbook: Ch. 5 §5.6, pp. 276 onward; Ch. 8 §8.3, pp. 506–511
ELEC 335 | L21 | Week 12
3
01
Map inputs to ROM addresses and output words
02
Build shared product terms in a PLA
03
Explain fixed OR allocation in a PAL
Course outcome: ROM, PLA and PAL circuit design
Notes: ELEC 335 | Lecture 21 | Week 12
Learning outcomes
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 5 §5.6, pp. 276 onward; Ch. 8 §8.3, pp. 506–511.
Companion animation: lesson-07.html
Map inputs to ROM addresses and output words
Build shared product terms in a PLA
Explain fixed OR allocation in a PAL

## Slide 4
L21 · BIG PICTURE
The question that organizes today
Textbook: Ch. 5 §5.6, pp. 276 onward; Ch. 8 §8.3, pp. 506–511
ELEC 335 | L21 | Week 12
4
How can one truth table be realized with three programmable structures?
Keep this question in view as the circuit models and examples develop.
Notes: ELEC 335 | Lecture 21 | Week 12
Guiding question
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 5 §5.6, pp. 276 onward; Ch. 8 §8.3, pp. 506–511.
Companion animation: lesson-07.html
Ask students for an initial answer: How can one truth table be realized with three programmable structures?

## Slide 5
L21 · PREREQUISITE BRIDGE
Start from what you already know
Textbook: Ch. 5 §5.6, pp. 276 onward; Ch. 8 §8.3, pp. 506–511
ELEC 335 | L21 | Week 12
5
✓
A truth table assigns output values to input combinations.
✓
A decoder selects one minterm from an address.
✓
Product terms can be shared across multiple output functions.
Turn to a partner: explain one statement without reading it aloud.
Notes: ELEC 335 | Lecture 21 | Week 12
Prerequisite bridge
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 5 §5.6, pp. 276 onward; Ch. 8 §8.3, pp. 506–511.
Companion animation: lesson-07.html
A truth table assigns output values to input combinations.
A decoder selects one minterm from an address.
Product terms can be shared across multiple output functions.

## Slide 6
L21 · VOCABULARY
Four words to make precise
Textbook: Ch. 5 §5.6, pp. 276 onward; Ch. 8 §8.3, pp. 506–511
ELEC 335 | L21 | Week 12
6
ROM
addressed store of complete output words
PLA
programmable AND and OR connections
PAL
programmable AND plane with fixed OR allocation
product term
AND of literals used in a sum-of-products form
Use each term when explaining the circuit, table, or timing trace.
Notes: ELEC 335 | Lecture 21 | Week 12
Vocabulary
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 5 §5.6, pp. 276 onward; Ch. 8 §8.3, pp. 506–511.
Companion animation: lesson-07.html
ROM: addressed store of complete output words
PLA: programmable AND and OR connections
PAL: programmable AND plane with fixed OR allocation
product term: AND of literals used in a sum-of-products form

## Slide 7
L21 · PLAIN-LANGUAGE MODEL
The reasoning sequence
Textbook: Ch. 5 §5.6, pp. 276 onward; Ch. 8 §8.3, pp. 506–511
ELEC 335 | L21 | Week 12
7
01
List every address and required output word.
02
Identify shared product terms for a PLA.
03
Check the available OR allocation for a PAL.
How can one truth table be realized with three programmable structures?
Notes: ELEC 335 | Lecture 21 | Week 12
Plain-language model
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 5 §5.6, pp. 276 onward; Ch. 8 §8.3, pp. 506–511.
Companion animation: lesson-07.html
List every address and required output word.
Identify shared product terms for a PLA.
Check the available OR allocation for a PAL.

## Slide 8
L21 · REFERENCE
The table to keep beside the method
Textbook: Ch. 5 §5.6, pp. 276 onward; Ch. 8 §8.3, pp. 506–511
ELEC 335 | L21 | Week 12
8
A B | ROM word F G | Active product
0 0 | 0 0 | none
0 1 | 1 0 | A′B
1 0 | 1 0 | AB′
1 1 | 0 1 | AB
Name the bit order and control conditions before using a row.
Notes: ELEC 335 | Lecture 21 | Week 12
Reference table
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 5 §5.6, pp. 276 onward; Ch. 8 §8.3, pp. 506–511.
Companion animation: lesson-07.html
Read all columns in the bit order shown. Ask students to predict one row before the worked example.

## Slide 9
L21 · METHOD
A reliable procedure for exercises
Textbook: Ch. 5 §5.6, pp. 276 onward; Ch. 8 §8.3, pp. 506–511
ELEC 335 | L21 | Week 12
9
1
Write the full input/output truth table with a fixed address order.
2
For ROM, copy output words into addresses; for PLA, minimize and list product terms.
3
For PAL, allocate product terms to each fixed output OR and check device limits.
Complete the table or trace, then verify the circuit one row at a time.
Notes: ELEC 335 | Lecture 21 | Week 12
Textbook exercise method
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 5 §5.6, pp. 276 onward; Ch. 8 §8.3, pp. 506–511.
Companion animation: lesson-07.html
Write the full input/output truth table with a fixed address order.
For ROM, copy output words into addresses; for PLA, minimize and list product terms.
For PAL, allocate product terms to each fixed output OR and check device limits.

## Slide 10
L21 · WORKED EXAMPLE
Implement XOR and AND
Textbook: Ch. 5 §5.6, pp. 276 onward; Ch. 8 §8.3, pp. 506–511
ELEC 335 | L21 | Week 12
10
Let F=A⊕B and G=AB. Realize both functions by ROM and PLA.
1
List output words at addresses 00,01,10,11: 00,10,10,01.
2
A 4×2 ROM stores those four words.
3
Form PLA terms P₁=A′B, P₂=AB′ and P₃=AB.
4
Connect F=P₁+P₂ and G=P₃.
The ROM stores 8 output bits. The PLA uses three product terms for this direct SOP realization.
Notes: ELEC 335 | Lecture 21 | Week 12
Implement XOR and AND
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 5 §5.6, pp. 276 onward; Ch. 8 §8.3, pp. 506–511.
Companion animation: lesson-07.html
Prompt: Let F=A⊕B and G=AB. Realize both functions by ROM and PLA.
Steps:
List output words at addresses 00,01,10,11: 00,10,10,01.
A 4×2 ROM stores those four words.
Form PLA terms P₁=A′B, P₂=AB′ and P₃=AB.
Connect F=P₁+P₂ and G=P₃.
Answer: The ROM stores 8 output bits. The PLA uses three product terms for this direct SOP realization.

## Slide 11
L21 · CONCEPT
Two designs to distinguish
Textbook: Ch. 5 §5.6, pp. 276 onward; Ch. 8 §8.3, pp. 506–511
ELEC 335 | L21 | Week 12
11
ROM
Stores one word for every input address.
Direct table implementation.
PLA / PAL
Implements selected product terms.
Economical when expressions are sparse or shared.
Explain the difference using behavior and timing, then test one case.
Notes: ELEC 335 | Lecture 21 | Week 12
Concept comparison
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 5 §5.6, pp. 276 onward; Ch. 8 §8.3, pp. 506–511.
Companion animation: lesson-07.html
ROM | Stores one word for every input address. | Direct table implementation.
PLA / PAL | Implements selected product terms. | Economical when expressions are sparse or shared.

## Slide 12
L21 · INTERACTIVE COMPANION
One function, three architectures
Textbook: Ch. 5 §5.6, pp. 276 onward; Ch. 8 §8.3, pp. 506–511
ELEC 335 | L21 | Week 12
12
A, B
→
ROM 4 × 2
→
F, G
Compare the ROM table with PLA and PAL product terms
Select A and B. The highlighted address, product term and outputs update together.
Open lesson-07.html for the animated model and state-by-state controls.
Notes: ELEC 335 | Lecture 21 | Week 12
Interactive model
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 5 §5.6, pp. 276 onward; Ch. 8 §8.3, pp. 506–511.
Companion animation: lesson-07.html
Select A and B. The highlighted address, product term and outputs update together.
Toggle the address and have students read the ROM word before exposing equations.
Highlight how the same truth table maps to a PLA product plane.
Ask students to count terms required at each PAL output.

## Slide 13
ACTIVITY
L21
TEAM
TASK
Apply the method together
Given two functions of A and B, write a four-address ROM table and identify product terms that could be shared in a PLA.
Write the full input/output truth table with a fixed address order.
DELIVERABLE
A four-row ROM map and a labelled sum-of-products implementation.
Textbook: Ch. 5 §5.6, pp. 276 onward; Ch. 8 §8.3, pp. 506–511
L21 | Week 12
ELEC 335 | Digital Logic Design
13
Notes: ELEC 335 | Lecture 21 | Week 12
Team activity
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 5 §5.6, pp. 276 onward; Ch. 8 §8.3, pp. 506–511.
Companion animation: lesson-07.html
Given two functions of A and B, write a four-address ROM table and identify product terms that could be shared in a PLA.
Deliverable: A four-row ROM map and a labelled sum-of-products implementation.

## Slide 14
L21 · GUIDED EXAMPLE
Try the first move before I do
Textbook: Ch. 5 §5.6, pp. 276 onward; Ch. 8 §8.3, pp. 506–511
ELEC 335 | L21 | Week 12
14
A PAL gives each output two fixed OR inputs. Can the same XOR/AND pair fit?
YOUR FIRST MOVE
F needs two product terms, A′B and AB′.
Pause for 60–90 seconds. Write, then compare with a partner.
Notes: ELEC 335 | Lecture 21 | Week 12
Guided example
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 5 §5.6, pp. 276 onward; Ch. 8 §8.3, pp. 506–511.
Companion animation: lesson-07.html
Prompt: A PAL gives each output two fixed OR inputs. Can the same XOR/AND pair fit?
First move: F needs two product terms, A′B and AB′.
Pause before showing the next slide.

## Slide 15
L21 · GUIDED SOLUTION
Now make every step visible
Textbook: Ch. 5 §5.6, pp. 276 onward; Ch. 8 §8.3, pp. 506–511
ELEC 335 | L21 | Week 12
15
1
F needs two product terms, A′B and AB′.
2
G needs one product term, AB.
3
Allocate two AND terms to F and one to G.
4
Check the actual PAL for available true/complement input literals and output polarity.
It fits this stated two-terms-per-output model; a real device must be checked against its data sheet.
Notes: ELEC 335 | Lecture 21 | Week 12
Assess a PAL fit
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 5 §5.6, pp. 276 onward; Ch. 8 §8.3, pp. 506–511.
Companion animation: lesson-07.html
Steps:
F needs two product terms, A′B and AB′.
G needs one product term, AB.
Allocate two AND terms to F and one to G.
Check the actual PAL for available true/complement input literals and output polarity.
Answer: It fits this stated two-terms-per-output model; a real device must be checked against its data sheet.

## Slide 16
L21 · MISCONCEPTION CLINIC
A tempting mistake to remove now
Textbook: Ch. 5 §5.6, pp. 276 onward; Ch. 8 §8.3, pp. 506–511
ELEC 335 | L21 | Week 12
16
TEMPTING CLAIM
ROM, PLA and PAL all store a complete truth table in the same way.
WHY IT FAILS
A ROM stores addressable words, while a PLA or PAL implements product terms.
REPAIR
Compare the address map with the chosen product-term connections.
Notes: ELEC 335 | Lecture 21 | Week 12
Misconception clinic
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 5 §5.6, pp. 276 onward; Ch. 8 §8.3, pp. 506–511.
Companion animation: lesson-07.html
TEMPTING CLAIM: ROM, PLA and PAL all store a complete truth table in the same way.
WHY IT FAILS: A ROM stores addressable words, while a PLA or PAL implements product terms.
REPAIR: Compare the address map with the chosen product-term connections.

## Slide 17
L21 · ONE-MINUTE CHECKS
Close the book: can you apply it?
Textbook: Ch. 5 §5.6, pp. 276 onward; Ch. 8 §8.3, pp. 506–511
ELEC 335 | L21 | Week 12
17
Q1
For two input bits and three output bits, what is the minimum ROM organization?
Q2
Let H=A+B. Which input rows store H=1?
Answer without notes, then compare your reasoning with the next slide.
Notes: ELEC 335 | Lecture 21 | Week 12
Practice questions
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 5 §5.6, pp. 276 onward; Ch. 8 §8.3, pp. 506–511.
Companion animation: lesson-07.html
Q1: For two input bits and three output bits, what is the minimum ROM organization?
Hint: Addresses are all input combinations.
Answer: 4×3, meaning four addresses and three output bits per word.
Q2: Let H=A+B. Which input rows store H=1?
Hint: OR is 0 only when both inputs are 0.
Answer: Addresses 01, 10 and 11.

## Slide 18
L21 · PRACTICE SOLUTIONS
Check the rule behind each answer
Textbook: Ch. 5 §5.6, pp. 276 onward; Ch. 8 §8.3, pp. 506–511
ELEC 335 | L21 | Week 12
18
Q1
4×3, meaning four addresses and three output bits per word.
Q2
Addresses 01, 10 and 11.
Return to the reference table if your answer used a different rule.
Notes: ELEC 335 | Lecture 21 | Week 12
Practice solutions
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 5 §5.6, pp. 276 onward; Ch. 8 §8.3, pp. 506–511.
Companion animation: lesson-07.html
Q1: For two input bits and three output bits, what is the minimum ROM organization?
4×3, meaning four addresses and three output bits per word.
Q2: Let H=A+B. Which input rows store H=1?
Addresses 01, 10 and 11.

## Slide 19
L21 · CLOSE
What should stay with you
Textbook: Ch. 5 §5.6, pp. 276 onward; Ch. 8 §8.3, pp. 506–511
ELEC 335 | L21 | Week 12
19
Map inputs to ROM addresses and output words
Build shared product terms in a PLA
Explain fixed OR allocation in a PAL
NEXT
Next: State reduction by implication. Use lesson-08.html to preview its model.
Notes: ELEC 335 | Lecture 21 | Week 12
Closing outcomes
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 5 §5.6, pp. 276 onward; Ch. 8 §8.3, pp. 506–511.
Companion animation: lesson-07.html
Map inputs to ROM addresses and output words
Build shared product terms in a PLA
Explain fixed OR allocation in a PAL
Next companion: lesson-08.html