## Slide 1
ELEC 335 | Fall 2026
State reduction by implication
Week 12 · Lecture 2
Chapter 9
Digital Logic Design
Textbook: Ch. 9 §9.1, online chapter pp. 9-3–9-10
Notes: ELEC 335 | Lecture 22 | Week 12
Opening
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 9 §9.1, online chapter pp. 9-3–9-10.
Companion animation: lesson-08.html
Opening question: When are two states indistinguishable for every future input sequence?
Outcomes: Mark output-incompatible state pairs | Propagate successor implications | Construct a reduced machine from unmarked pairs

## Slide 2
L22 · READING MAP
Where this lecture sits in the course
Textbook: Ch. 9 §9.1, online chapter pp. 9-3–9-10
ELEC 335 | L22 | Week 12
2
1
Textbook: Ch. 9 §9.1, online chapter pp. 9-3–9-10
2
Interactive companion: Lesson 08, State reduction by implication
3
After class: worked examples and practice in the HTML lesson
Preparation: read the named section, then use the worked slides to check each design step.
Notes: ELEC 335 | Lecture 22 | Week 12
Reading map
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 9 §9.1, online chapter pp. 9-3–9-10.
Companion animation: lesson-08.html

## Slide 3
L22 · LEARNING OUTCOMES
Today's destination
Textbook: Ch. 9 §9.1, online chapter pp. 9-3–9-10
ELEC 335 | L22 | Week 12
3
01
Mark output-incompatible state pairs
02
Propagate successor implications
03
Construct a reduced machine from unmarked pairs
Course outcome: State tables and efficient sequential design
Notes: ELEC 335 | Lecture 22 | Week 12
Learning outcomes
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 9 §9.1, online chapter pp. 9-3–9-10.
Companion animation: lesson-08.html
Mark output-incompatible state pairs
Propagate successor implications
Construct a reduced machine from unmarked pairs

## Slide 4
L22 · BIG PICTURE
The question that organizes today
Textbook: Ch. 9 §9.1, online chapter pp. 9-3–9-10
ELEC 335 | L22 | Week 12
4
When are two states indistinguishable for every future input sequence?
Keep this question in view as the circuit models and examples develop.
Notes: ELEC 335 | Lecture 22 | Week 12
Guiding question
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 9 §9.1, online chapter pp. 9-3–9-10.
Companion animation: lesson-08.html
Ask students for an initial answer: When are two states indistinguishable for every future input sequence?

## Slide 5
L22 · PREREQUISITE BRIDGE
Start from what you already know
Textbook: Ch. 9 §9.1, online chapter pp. 9-3–9-10
ELEC 335 | L22 | Week 12
5
✓
A state table supplies output and successor information.
✓
Equivalent states have the same external behavior.
✓
A difference in output prevents equivalence immediately.
Turn to a partner: explain one statement without reading it aloud.
Notes: ELEC 335 | Lecture 22 | Week 12
Prerequisite bridge
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 9 §9.1, online chapter pp. 9-3–9-10.
Companion animation: lesson-08.html
A state table supplies output and successor information.
Equivalent states have the same external behavior.
A difference in output prevents equivalence immediately.

## Slide 6
L22 · VOCABULARY
Four words to make precise
Textbook: Ch. 9 §9.1, online chapter pp. 9-3–9-10
ELEC 335 | L22 | Week 12
6
equivalent states
states with identical observable behavior for every input sequence
implication pair
successor pair that must also be equivalent
incompatible pair
pair proved distinguishable
reduced machine
machine after equivalent states are merged
Use each term when explaining the circuit, table, or timing trace.
Notes: ELEC 335 | Lecture 22 | Week 12
Vocabulary
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 9 §9.1, online chapter pp. 9-3–9-10.
Companion animation: lesson-08.html
equivalent states: states with identical observable behavior for every input sequence
implication pair: successor pair that must also be equivalent
incompatible pair: pair proved distinguishable
reduced machine: machine after equivalent states are merged

## Slide 7
L22 · PLAIN-LANGUAGE MODEL
The reasoning sequence
Textbook: Ch. 9 §9.1, online chapter pp. 9-3–9-10
ELEC 335 | L22 | Week 12
7
01
Mark pairs whose outputs differ.
02
For each remaining pair, record successor implications.
03
Propagate incompatibility until no new pair is marked.
When are two states indistinguishable for every future input sequence?
Notes: ELEC 335 | Lecture 22 | Week 12
Plain-language model
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 9 §9.1, online chapter pp. 9-3–9-10.
Companion animation: lesson-08.html
Mark pairs whose outputs differ.
For each remaining pair, record successor implications.
Propagate incompatibility until no new pair is marked.

## Slide 8
L22 · REFERENCE
The table to keep beside the method
Textbook: Ch. 9 §9.1, online chapter pp. 9-3–9-10
ELEC 335 | L22 | Week 12
8
State / output | X=0 next | X=1 next
A / 0 | B | C
B / 0 | B | D
C / 0 | C | D
D / 1 | D | D
Name the bit order and control conditions before using a row.
Notes: ELEC 335 | Lecture 22 | Week 12
Reference table
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 9 §9.1, online chapter pp. 9-3–9-10.
Companion animation: lesson-08.html
Read all columns in the bit order shown. Ask students to predict one row before the worked example.

## Slide 9
L22 · METHOD
A reliable procedure for exercises
Textbook: Ch. 9 §9.1, online chapter pp. 9-3–9-10
ELEC 335 | L22 | Week 12
9
1
List all unordered pairs and mark immediate output conflicts.
2
Record successor-pair implications for each remaining pair and propagate marks to a fixed point.
3
Merge only unmarked equivalence classes and rebuild the transition table.
Complete the table or trace, then verify the circuit one row at a time.
Notes: ELEC 335 | Lecture 22 | Week 12
Textbook exercise method
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 9 §9.1, online chapter pp. 9-3–9-10.
Companion animation: lesson-08.html
List all unordered pairs and mark immediate output conflicts.
Record successor-pair implications for each remaining pair and propagate marks to a fixed point.
Merge only unmarked equivalence classes and rebuild the transition table.

## Slide 10
L22 · WORKED EXAMPLE
Reduce a four-state Moore machine
Textbook: Ch. 9 §9.1, online chapter pp. 9-3–9-10
ELEC 335 | L22 | Week 12
10
Use the table above. Determine which states can be merged.
1
Mark (A,D), (B,D) and (C,D): their present outputs differ.
2
Pair (A,B) implies (B,B) for X=0 and (C,D) for X=1. Since (C,D) is marked, mark (A,B).
3
Pair (A,C) implies (B,C) for X=0 and (C,D) for X=1, so mark (A,C).
4
Pair (B,C) implies itself for X=0 and (D,D) for X=1, so it remains unmarked.
Merge B and C. The reduced states are {A}, {B,C} and {D}.
Notes: ELEC 335 | Lecture 22 | Week 12
Reduce a four-state Moore machine
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 9 §9.1, online chapter pp. 9-3–9-10.
Companion animation: lesson-08.html
Prompt: Use the table above. Determine which states can be merged.
Steps:
Mark (A,D), (B,D) and (C,D): their present outputs differ.
Pair (A,B) implies (B,B) for X=0 and (C,D) for X=1. Since (C,D) is marked, mark (A,B).
Pair (A,C) implies (B,C) for X=0 and (C,D) for X=1, so mark (A,C).
Pair (B,C) implies itself for X=0 and (D,D) for X=1, so it remains unmarked.
Answer: Merge B and C. The reduced states are {A}, {B,C} and {D}.

## Slide 11
L22 · CONCEPT
Two designs to distinguish
Textbook: Ch. 9 §9.1, online chapter pp. 9-3–9-10
ELEC 335 | L22 | Week 12
11
Immediate mark
Outputs differ for the same input.
No successor analysis is needed.
Implied mark
A successor pair is already incompatible.
The distinction propagates backward.
Explain the difference using behavior and timing, then test one case.
Notes: ELEC 335 | Lecture 22 | Week 12
Concept comparison
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 9 §9.1, online chapter pp. 9-3–9-10.
Companion animation: lesson-08.html
Immediate mark | Outputs differ for the same input. | No successor analysis is needed.
Implied mark | A successor pair is already incompatible. | The distinction propagates backward.

## Slide 12
L22 · INTERACTIVE COMPANION
Implication-table animator
Textbook: Ch. 9 §9.1, online chapter pp. 9-3–9-10
ELEC 335 | L22 | Week 12
12
Pair (A,B)
→
Pair (C,D)
A successor distinction propagates backward
Advance one pass at a time. Immediate output mismatches appear first; successor distinctions propagate next.
Open lesson-08.html for the animated model and state-by-state controls.
Notes: ELEC 335 | Lecture 22 | Week 12
Interactive model
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 9 §9.1, online chapter pp. 9-3–9-10.
Companion animation: lesson-08.html
Advance one pass at a time. Immediate output mismatches appear first; successor distinctions propagate next.
Stop after the first pass and ask whether A and B can now be merged.
Advance the propagation pass and trace the single distinguishing input.
Have students rebuild the reduced table from equivalence classes.

## Slide 13
ACTIVITY
L22
TEAM
TASK
Apply the method together
Use the lesson’s state table to mark output-incompatible pairs, record one successor implication, and identify a pair that survives.
List all unordered pairs and mark immediate output conflicts.
DELIVERABLE
A completed implication chart and proposed reduced-state groups.
Textbook: Ch. 9 §9.1, online chapter pp. 9-3–9-10
L22 | Week 12
ELEC 335 | Digital Logic Design
13
Notes: ELEC 335 | Lecture 22 | Week 12
Team activity
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 9 §9.1, online chapter pp. 9-3–9-10.
Companion animation: lesson-08.html
Use the lesson’s state table to mark output-incompatible pairs, record one successor implication, and identify a pair that survives.
Deliverable: A completed implication chart and proposed reduced-state groups.

## Slide 14
L22 · GUIDED EXAMPLE
Try the first move before I do
Textbook: Ch. 9 §9.1, online chapter pp. 9-3–9-10
ELEC 335 | L22 | Week 12
14
States A and B both output 0. Explain why they are still distinguishable.
YOUR FIRST MOVE
Apply input X=1.
Pause for 60–90 seconds. Write, then compare with a partner.
Notes: ELEC 335 | Lecture 22 | Week 12
Guided example
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 9 §9.1, online chapter pp. 9-3–9-10.
Companion animation: lesson-08.html
Prompt: States A and B both output 0. Explain why they are still distinguishable.
First move: Apply input X=1.
Pause before showing the next slide.

## Slide 15
L22 · GUIDED SOLUTION
Now make every step visible
Textbook: Ch. 9 §9.1, online chapter pp. 9-3–9-10
ELEC 335 | L22 | Week 12
15
1
Apply input X=1.
2
A moves to C, whose output is 0.
3
B moves to D, whose output is 1.
The one-symbol input sequence 1 distinguishes A from B on the following state interval.
Notes: ELEC 335 | Lecture 22 | Week 12
Show why same output is insufficient
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 9 §9.1, online chapter pp. 9-3–9-10.
Companion animation: lesson-08.html
Steps:
Apply input X=1.
A moves to C, whose output is 0.
B moves to D, whose output is 1.
Answer: The one-symbol input sequence 1 distinguishes A from B on the following state interval.

## Slide 16
L22 · MISCONCEPTION CLINIC
A tempting mistake to remove now
Textbook: Ch. 9 §9.1, online chapter pp. 9-3–9-10
ELEC 335 | L22 | Week 12
16
TEMPTING CLAIM
States with the same current output are always equivalent.
WHY IT FAILS
A later input may send them to distinguishable successor states.
REPAIR
Propagate successor implications before merging states.
Notes: ELEC 335 | Lecture 22 | Week 12
Misconception clinic
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 9 §9.1, online chapter pp. 9-3–9-10.
Companion animation: lesson-08.html
TEMPTING CLAIM: States with the same current output are always equivalent.
WHY IT FAILS: A later input may send them to distinguishable successor states.
REPAIR: Propagate successor implications before merging states.

## Slide 17
L22 · ONE-MINUTE CHECKS
Close the book: can you apply it?
Textbook: Ch. 9 §9.1, online chapter pp. 9-3–9-10
ELEC 335 | L22 | Week 12
17
Q1
Which pairs are marked before considering successor states?
Q2
What is the reduced transition from {B,C} when X=0?
Answer without notes, then compare your reasoning with the next slide.
Notes: ELEC 335 | Lecture 22 | Week 12
Practice questions
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 9 §9.1, online chapter pp. 9-3–9-10.
Companion animation: lesson-08.html
Q1: Which pairs are marked before considering successor states?
Hint: Compare the output column.
Answer: (A,D), (B,D) and (C,D).
Q2: What is the reduced transition from {B,C} when X=0?
Hint: Check both B and C destinations.
Answer: Both destinations remain in {B,C}, so the reduced transition is a self-loop.

## Slide 18
L22 · PRACTICE SOLUTIONS
Check the rule behind each answer
Textbook: Ch. 9 §9.1, online chapter pp. 9-3–9-10
ELEC 335 | L22 | Week 12
18
Q1
(A,D), (B,D) and (C,D).
Q2
Both destinations remain in {B,C}, so the reduced transition is a self-loop.
Return to the reference table if your answer used a different rule.
Notes: ELEC 335 | Lecture 22 | Week 12
Practice solutions
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 9 §9.1, online chapter pp. 9-3–9-10.
Companion animation: lesson-08.html
Q1: Which pairs are marked before considering successor states?
(A,D), (B,D) and (C,D).
Q2: What is the reduced transition from {B,C} when X=0?
Both destinations remain in {B,C}, so the reduced transition is a self-loop.

## Slide 19
L22 · CLOSE
What should stay with you
Textbook: Ch. 9 §9.1, online chapter pp. 9-3–9-10
ELEC 335 | L22 | Week 12
19
Mark output-incompatible state pairs
Propagate successor implications
Construct a reduced machine from unmarked pairs
NEXT
Next: Partitions and state assignment. Use lesson-09.html to preview its model.
Notes: ELEC 335 | Lecture 22 | Week 12
Closing outcomes
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 9 §9.1, online chapter pp. 9-3–9-10.
Companion animation: lesson-08.html
Mark output-incompatible state pairs
Propagate successor implications
Construct a reduced machine from unmarked pairs
Next companion: lesson-09.html