## Slide 1
ELEC 335 | Fall 2026
Partitions and state assignment
Week 13 · Lecture 1
Chapter 9
Digital Logic Design
Textbook: Ch. 9 §§9.2–9.4, online chapter pp. 9-10–9-28
Notes: ELEC 335 | Lecture 23 | Week 13
Opening
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 9 §§9.2–9.4, online chapter pp. 9-10–9-28.
Companion animation: lesson-09.html
Opening question: How do we separate behavioral reduction from binary coding?
Outcomes: Refine an output partition to stability | Assign codes after reduction | Compare binary and one-hot implementation costs

## Slide 2
L23 · READING MAP
Where this lecture sits in the course
Textbook: Ch. 9 §§9.2–9.4, online chapter pp. 9-10–9-28
ELEC 335 | L23 | Week 13
2
1
Textbook: Ch. 9 §§9.2–9.4, online chapter pp. 9-10–9-28
2
Interactive companion: Lesson 09, Partitions and state assignment
3
After class: worked examples and practice in the HTML lesson
Preparation: read the named section, then use the worked slides to check each design step.
Notes: ELEC 335 | Lecture 23 | Week 13
Reading map
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 9 §§9.2–9.4, online chapter pp. 9-10–9-28.
Companion animation: lesson-09.html

## Slide 3
L23 · LEARNING OUTCOMES
Today's destination
Textbook: Ch. 9 §§9.2–9.4, online chapter pp. 9-10–9-28
ELEC 335 | L23 | Week 13
3
01
Refine an output partition to stability
02
Assign codes after reduction
03
Compare binary and one-hot implementation costs
Course outcome: State reduction and state assignment
Notes: ELEC 335 | Lecture 23 | Week 13
Learning outcomes
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 9 §§9.2–9.4, online chapter pp. 9-10–9-28.
Companion animation: lesson-09.html
Refine an output partition to stability
Assign codes after reduction
Compare binary and one-hot implementation costs

## Slide 4
L23 · BIG PICTURE
The question that organizes today
Textbook: Ch. 9 §§9.2–9.4, online chapter pp. 9-10–9-28
ELEC 335 | L23 | Week 13
4
How do we separate behavioral reduction from binary coding?
Keep this question in view as the circuit models and examples develop.
Notes: ELEC 335 | Lecture 23 | Week 13
Guiding question
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 9 §§9.2–9.4, online chapter pp. 9-10–9-28.
Companion animation: lesson-09.html
Ask students for an initial answer: How do we separate behavioral reduction from binary coding?

## Slide 5
L23 · PREREQUISITE BRIDGE
Start from what you already know
Textbook: Ch. 9 §§9.2–9.4, online chapter pp. 9-10–9-28
ELEC 335 | L23 | Week 13
5
✓
Output behavior gives an initial partition.
✓
States in a block must stay compatible under every input.
✓
State codes are chosen only after the number of states is known.
Turn to a partner: explain one statement without reading it aloud.
Notes: ELEC 335 | Lecture 23 | Week 13
Prerequisite bridge
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 9 §§9.2–9.4, online chapter pp. 9-10–9-28.
Companion animation: lesson-09.html
Output behavior gives an initial partition.
States in a block must stay compatible under every input.
State codes are chosen only after the number of states is known.

## Slide 6
L23 · VOCABULARY
Four words to make precise
Textbook: Ch. 9 §§9.2–9.4, online chapter pp. 9-10–9-28
ELEC 335 | L23 | Week 13
6
partition
grouping of states with the same current signature
refinement
splitting a block by successor blocks
stable partition
partition that no longer splits
state assignment
binary or one-hot codes chosen for final states
Use each term when explaining the circuit, table, or timing trace.
Notes: ELEC 335 | Lecture 23 | Week 13
Vocabulary
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 9 §§9.2–9.4, online chapter pp. 9-10–9-28.
Companion animation: lesson-09.html
partition: grouping of states with the same current signature
refinement: splitting a block by successor blocks
stable partition: partition that no longer splits
state assignment: binary or one-hot codes chosen for final states

## Slide 7
L23 · PLAIN-LANGUAGE MODEL
The reasoning sequence
Textbook: Ch. 9 §§9.2–9.4, online chapter pp. 9-10–9-28
ELEC 335 | L23 | Week 13
7
01
Group states by outputs.
02
Split any block with different destination-block signatures.
03
Repeat to stability, then choose an encoding.
How do we separate behavioral reduction from binary coding?
Notes: ELEC 335 | Lecture 23 | Week 13
Plain-language model
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 9 §§9.2–9.4, online chapter pp. 9-10–9-28.
Companion animation: lesson-09.html
Group states by outputs.
Split any block with different destination-block signatures.
Repeat to stability, then choose an encoding.

## Slide 8
L23 · REFERENCE
The table to keep beside the method
Textbook: Ch. 9 §§9.2–9.4, online chapter pp. 9-10–9-28
ELEC 335 | L23 | Week 13
8
Pass | Partition
P₀ (output) | {A,B,C} ¦ {D}
P₁ (successor signatures) | {A} ¦ {B,C} ¦ {D}
P₂ | No further split: stable
Name the bit order and control conditions before using a row.
Notes: ELEC 335 | Lecture 23 | Week 13
Reference table
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 9 §§9.2–9.4, online chapter pp. 9-10–9-28.
Companion animation: lesson-09.html
Read all columns in the bit order shown. Ask students to predict one row before the worked example.

## Slide 9
L23 · METHOD
A reliable procedure for exercises
Textbook: Ch. 9 §§9.2–9.4, online chapter pp. 9-10–9-28
ELEC 335 | L23 | Week 13
9
1
Partition states by observable output, then calculate destination-block signatures.
2
Split blocks with unequal signatures until the partition stops changing.
3
Assign codes to stable classes and compare complete logic and reset costs.
Complete the table or trace, then verify the circuit one row at a time.
Notes: ELEC 335 | Lecture 23 | Week 13
Textbook exercise method
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 9 §§9.2–9.4, online chapter pp. 9-10–9-28.
Companion animation: lesson-09.html
Partition states by observable output, then calculate destination-block signatures.
Split blocks with unequal signatures until the partition stops changing.
Assign codes to stable classes and compare complete logic and reset costs.

## Slide 10
L23 · WORKED EXAMPLE
Refine the four-state example
Textbook: Ch. 9 §§9.2–9.4, online chapter pp. 9-10–9-28
ELEC 335 | L23 | Week 13
10
Use the state table from Lesson 08. Start with groups of equal Moore output.
1
P₀={{A,B,C},{D}}.
2
Within {A,B,C}, inspect destination blocks for X=0 and X=1.
3
A has signature ({A,B,C},{A,B,C}); B and C have ({A,B,C},{D}).
4
Split A from {B,C}. Repeating produces no further split.
Stable classes are {A}, {B,C}, {D}.
Notes: ELEC 335 | Lecture 23 | Week 13
Refine the four-state example
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 9 §§9.2–9.4, online chapter pp. 9-10–9-28.
Companion animation: lesson-09.html
Prompt: Use the state table from Lesson 08. Start with groups of equal Moore output.
Steps:
P₀={{A,B,C},{D}}.
Within {A,B,C}, inspect destination blocks for X=0 and X=1.
A has signature ({A,B,C},{A,B,C}); B and C have ({A,B,C},{D}).
Split A from {B,C}. Repeating produces no further split.
Answer: Stable classes are {A}, {B,C}, {D}.

## Slide 11
L23 · CONCEPT
Two designs to distinguish
Textbook: Ch. 9 §§9.2–9.4, online chapter pp. 9-10–9-28
ELEC 335 | L23 | Week 13
11
Binary assignment
Uses fewer storage bits.
Usually needs explicit decoding.
One-hot assignment
Uses one bit per state.
Often simplifies transition logic.
Explain the difference using behavior and timing, then test one case.
Notes: ELEC 335 | Lecture 23 | Week 13
Concept comparison
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 9 §§9.2–9.4, online chapter pp. 9-10–9-28.
Companion animation: lesson-09.html
Binary assignment | Uses fewer storage bits. | Usually needs explicit decoding.
One-hot assignment | Uses one bit per state. | Often simplifies transition logic.

## Slide 12
L23 · INTERACTIVE COMPANION
Partition refinement and encoding
Textbook: Ch. 9 §§9.2–9.4, online chapter pp. 9-10–9-28
ELEC 335 | L23 | Week 13
12
{A,B,C} {D}
→
{A} {B,C} {D}
Refine until every block has one successor signature
Advance from output grouping to the stable partition. Then compare binary and one-hot state codes.
Open lesson-09.html for the animated model and state-by-state controls.
Notes: ELEC 335 | Lecture 23 | Week 13
Interactive model
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 9 §§9.2–9.4, online chapter pp. 9-10–9-28.
Companion animation: lesson-09.html
Advance from output grouping to the stable partition. Then compare binary and one-hot state codes.
Reveal P₀ and ask students to predict the first split.
Use destination signatures to justify the split.
Switch the displayed codes and emphasize that transitions stay the same.

## Slide 13
ACTIVITY
L23
TEAM
TASK
Apply the method together
Refine the lesson’s initial output partition once. Explain which destination signature separates the states in a split block.
Partition states by observable output, then calculate destination-block signatures.
DELIVERABLE
Before-and-after partitions and one justified split.
Textbook: Ch. 9 §§9.2–9.4, online chapter pp. 9-10–9-28
L23 | Week 13
ELEC 335 | Digital Logic Design
13
Notes: ELEC 335 | Lecture 23 | Week 13
Team activity
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 9 §§9.2–9.4, online chapter pp. 9-10–9-28.
Companion animation: lesson-09.html
Refine the lesson’s initial output partition once. Explain which destination signature separates the states in a split block.
Deliverable: Before-and-after partitions and one justified split.

## Slide 14
L23 · GUIDED EXAMPLE
Try the first move before I do
Textbook: Ch. 9 §§9.2–9.4, online chapter pp. 9-10–9-28
ELEC 335 | L23 | Week 13
14
Compare binary and one-hot codes for {A}, {B,C}, {D}.
YOUR FIRST MOVE
Binary needs two flip-flops. One assignment is 00, 01, 10.
Pause for 60–90 seconds. Write, then compare with a partner.
Notes: ELEC 335 | Lecture 23 | Week 13
Guided example
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 9 §§9.2–9.4, online chapter pp. 9-10–9-28.
Companion animation: lesson-09.html
Prompt: Compare binary and one-hot codes for {A}, {B,C}, {D}.
First move: Binary needs two flip-flops. One assignment is 00, 01, 10.
Pause before showing the next slide.

## Slide 15
L23 · GUIDED SOLUTION
Now make every step visible
Textbook: Ch. 9 §§9.2–9.4, online chapter pp. 9-10–9-28
ELEC 335 | L23 | Week 13
15
1
Binary needs two flip-flops. One assignment is 00, 01, 10.
2
One-hot needs three flip-flops. One assignment is 001, 010, 100.
3
Write the complete next-state table under each assignment.
4
Compare resulting logic and required recovery from invalid codes.
The assignment is an implementation choice; both must preserve the three-state transition behavior.
Notes: ELEC 335 | Lecture 23 | Week 13
Assign codes to three reduced states
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 9 §§9.2–9.4, online chapter pp. 9-10–9-28.
Companion animation: lesson-09.html
Steps:
Binary needs two flip-flops. One assignment is 00, 01, 10.
One-hot needs three flip-flops. One assignment is 001, 010, 100.
Write the complete next-state table under each assignment.
Compare resulting logic and required recovery from invalid codes.
Answer: The assignment is an implementation choice; both must preserve the three-state transition behavior.

## Slide 16
L23 · MISCONCEPTION CLINIC
A tempting mistake to remove now
Textbook: Ch. 9 §§9.2–9.4, online chapter pp. 9-10–9-28
ELEC 335 | L23 | Week 13
16
TEMPTING CLAIM
State codes should be assigned before equivalent states are merged.
WHY IT FAILS
Reduction can change the number of states and required bits.
REPAIR
Refine the partition to stability before assigning codes.
Notes: ELEC 335 | Lecture 23 | Week 13
Misconception clinic
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 9 §§9.2–9.4, online chapter pp. 9-10–9-28.
Companion animation: lesson-09.html
TEMPTING CLAIM: State codes should be assigned before equivalent states are merged.
WHY IT FAILS: Reduction can change the number of states and required bits.
REPAIR: Refine the partition to stability before assigning codes.

## Slide 17
L23 · ONE-MINUTE CHECKS
Close the book: can you apply it?
Textbook: Ch. 9 §§9.2–9.4, online chapter pp. 9-10–9-28
ELEC 335 | L23 | Week 13
17
Q1
How many flip-flops does binary encoding require for seven states?
Q2
Could A and B share one code if they have the same present output?
Answer without notes, then compare your reasoning with the next slide.
Notes: ELEC 335 | Lecture 23 | Week 13
Practice questions
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 9 §§9.2–9.4, online chapter pp. 9-10–9-28.
Companion animation: lesson-09.html
Q1: How many flip-flops does binary encoding require for seven states?
Hint: Find the smallest n with 2ⁿ≥7.
Answer: Three.
Q2: Could A and B share one code if they have the same present output?
Hint: Use the stable partition, not only P₀.
Answer: No. They occupy different stable classes because input 1 leads to different output behavior.

## Slide 18
L23 · PRACTICE SOLUTIONS
Check the rule behind each answer
Textbook: Ch. 9 §§9.2–9.4, online chapter pp. 9-10–9-28
ELEC 335 | L23 | Week 13
18
Q1
Three.
Q2
No. They occupy different stable classes because input 1 leads to different output behavior.
Return to the reference table if your answer used a different rule.
Notes: ELEC 335 | Lecture 23 | Week 13
Practice solutions
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 9 §§9.2–9.4, online chapter pp. 9-10–9-28.
Companion animation: lesson-09.html
Q1: How many flip-flops does binary encoding require for seven states?
Three.
Q2: Could A and B share one code if they have the same present output?
No. They occupy different stable classes because input 1 leads to different output behavior.

## Slide 19
L23 · CLOSE
What should stay with you
Textbook: Ch. 9 §§9.2–9.4, online chapter pp. 9-10–9-28
ELEC 335 | L23 | Week 13
19
Refine an output partition to stability
Assign codes after reduction
Compare binary and one-hot implementation costs
NEXT
Next: Integrated sequential design workshop. Use lesson-10.html to preview its model.
Notes: ELEC 335 | Lecture 23 | Week 13
Closing outcomes
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Ch. 9 §§9.2–9.4, online chapter pp. 9-10–9-28.
Companion animation: lesson-09.html
Refine an output partition to stability
Assign codes after reduction
Compare binary and one-hot implementation costs
Next companion: lesson-10.html