## Slide 1
ELEC 335 | Fall 2026
Integrated sequential design workshop
Week 13 · Lecture 2
Chapters 6–9 (review)
Digital Logic Design
Textbook: Review Ch. 6–9 and Ch. 5 §5.6
Notes: ELEC 335 | Lecture 24 | Week 13
Opening
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Review Ch. 6–9 and Ch. 5 §5.6.
Companion animation: lesson-10.html
Opening question: Can one design be traced from behavior to registers, state equations and a memory implementation?
Outcomes: Model a small serial transmitter as an FSM | Trace parallel load and serial shift timing | Map a controller table to ROM or product terms

## Slide 2
L24 · READING MAP
Where this lecture sits in the course
Textbook: Review Ch. 6–9 and Ch. 5 §5.6
ELEC 335 | L24 | Week 13
2
1
Textbook: Review Ch. 6–9 and Ch. 5 §5.6
2
Interactive companion: Lesson 10, Integrated sequential design workshop
3
After class: worked examples and practice in the HTML lesson
Preparation: read the named section, then use the worked slides to check each design step.
Notes: ELEC 335 | Lecture 24 | Week 13
Reading map
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Review Ch. 6–9 and Ch. 5 §5.6.
Companion animation: lesson-10.html

## Slide 3
L24 · LEARNING OUTCOMES
Today's destination
Textbook: Review Ch. 6–9 and Ch. 5 §5.6
ELEC 335 | L24 | Week 13
3
01
Model a small serial transmitter as an FSM
02
Trace parallel load and serial shift timing
03
Map a controller table to ROM or product terms
Course outcome: All three stated sequential and memory-device CLOs
Notes: ELEC 335 | Lecture 24 | Week 13
Learning outcomes
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Review Ch. 6–9 and Ch. 5 §5.6.
Companion animation: lesson-10.html
Model a small serial transmitter as an FSM
Trace parallel load and serial shift timing
Map a controller table to ROM or product terms

## Slide 4
L24 · BIG PICTURE
The question that organizes today
Textbook: Review Ch. 6–9 and Ch. 5 §5.6
ELEC 335 | L24 | Week 13
4
Can one design be traced from behavior to registers, state equations and a memory implementation?
Keep this question in view as the circuit models and examples develop.
Notes: ELEC 335 | Lecture 24 | Week 13
Guiding question
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Review Ch. 6–9 and Ch. 5 §5.6.
Companion animation: lesson-10.html
Ask students for an initial answer: Can one design be traced from behavior to registers, state equations and a memory implementation?

## Slide 5
L24 · PREREQUISITE BRIDGE
Start from what you already know
Textbook: Review Ch. 6–9 and Ch. 5 §5.6
ELEC 335 | L24 | Week 13
5
✓
A controller can be described by states and outputs.
✓
A register can parallel-load and serial-shift a word.
✓
A ROM can store next-state and output words.
Turn to a partner: explain one statement without reading it aloud.
Notes: ELEC 335 | Lecture 24 | Week 13
Prerequisite bridge
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Review Ch. 6–9 and Ch. 5 §5.6.
Companion animation: lesson-10.html
A controller can be described by states and outputs.
A register can parallel-load and serial-shift a word.
A ROM can store next-state and output words.

## Slide 6
L24 · VOCABULARY
Four words to make precise
Textbook: Review Ch. 6–9 and Ch. 5 §5.6
ELEC 335 | L24 | Week 13
6
datapath
registers and operations that carry data
controller
state logic that selects datapath operations
handshake
signals that coordinate start and completion
microoperation
register action during one control step
Use each term when explaining the circuit, table, or timing trace.
Notes: ELEC 335 | Lecture 24 | Week 13
Vocabulary
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Review Ch. 6–9 and Ch. 5 §5.6.
Companion animation: lesson-10.html
datapath: registers and operations that carry data
controller: state logic that selects datapath operations
handshake: signals that coordinate start and completion
microoperation: register action during one control step

## Slide 7
L24 · PLAIN-LANGUAGE MODEL
The reasoning sequence
Textbook: Review Ch. 6–9 and Ch. 5 §5.6
ELEC 335 | L24 | Week 13
7
01
Specify the external behavior and timing.
02
Separate datapath storage from control states.
03
Fill every state/input row, then map to logic or ROM.
Can one design be traced from behavior to registers, state equations and a memory implementation?
Notes: ELEC 335 | Lecture 24 | Week 13
Plain-language model
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Review Ch. 6–9 and Ch. 5 §5.6.
Companion animation: lesson-10.html
Specify the external behavior and timing.
Separate datapath storage from control states.
Fill every state/input row, then map to logic or ROM.

## Slide 8
L24 · REFERENCE
The table to keep beside the method
Textbook: Review Ch. 6–9 and Ch. 5 §5.6
ELEC 335 | L24 | Week 13
8
State | Condition | Next state | Action
IDLE | start=0 | IDLE | wait
IDLE | start=1 | LOAD | accept request
LOAD | any | SHIFT | parallel load; count←4
SHIFT | count>1 | SHIFT | emit bit; shift; decrement
SHIFT | count=1 | DONE | emit final bit
DONE | any | IDLE | done pulse
Name the bit order and control conditions before using a row.
Notes: ELEC 335 | Lecture 24 | Week 13
Reference table
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Review Ch. 6–9 and Ch. 5 §5.6.
Companion animation: lesson-10.html
Read all columns in the bit order shown. Ask students to predict one row before the worked example.

## Slide 9
L24 · METHOD
A reliable procedure for exercises
Textbook: Review Ch. 6–9 and Ch. 5 §5.6
ELEC 335 | L24 | Week 13
9
1
Separate controller state, datapath registers, inputs, and observable outputs.
2
Trace one clock edge at a time with state, count, data and output columns.
3
Build a complete controller table, specify invalid cases, then select gates or ROM/PLA/PAL implementation.
Complete the table or trace, then verify the circuit one row at a time.
Notes: ELEC 335 | Lecture 24 | Week 13
Textbook exercise method
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Review Ch. 6–9 and Ch. 5 §5.6.
Companion animation: lesson-10.html
Separate controller state, datapath registers, inputs, and observable outputs.
Trace one clock edge at a time with state, count, data and output columns.
Build a complete controller table, specify invalid cases, then select gates or ROM/PLA/PAL implementation.

## Slide 10
L24 · WORKED EXAMPLE
Trace transmission of 1011
Textbook: Review Ch. 6–9 and Ch. 5 §5.6
ELEC 335 | L24 | Week 13
10
The transmitter emits the rightmost bit first. Give the emitted sequence and number of SHIFT edges.
1
Start causes IDLE→LOAD; no bit is emitted yet.
2
LOAD captures 1011 and sets count to 4.
3
Four SHIFT edges emit 1,1,0,1.
4
After the fourth emission, state becomes DONE and count becomes 0.
The serial sequence is 1101 over four SHIFT edges.
Notes: ELEC 335 | Lecture 24 | Week 13
Trace transmission of 1011
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Review Ch. 6–9 and Ch. 5 §5.6.
Companion animation: lesson-10.html
Prompt: The transmitter emits the rightmost bit first. Give the emitted sequence and number of SHIFT edges.
Steps:
Start causes IDLE→LOAD; no bit is emitted yet.
LOAD captures 1011 and sets count to 4.
Four SHIFT edges emit 1,1,0,1.
After the fourth emission, state becomes DONE and count becomes 0.
Answer: The serial sequence is 1101 over four SHIFT edges.

## Slide 11
L24 · CONCEPT
Two designs to distinguish
Textbook: Review Ch. 6–9 and Ch. 5 §5.6
ELEC 335 | L24 | Week 13
11
Datapath
Holds and shifts the four-bit word.
Contains the register and bit count.
Controller
Chooses IDLE, LOAD, SHIFT, DONE.
Generates load, shift and done controls.
Explain the difference using behavior and timing, then test one case.
Notes: ELEC 335 | Lecture 24 | Week 13
Concept comparison
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Review Ch. 6–9 and Ch. 5 §5.6.
Companion animation: lesson-10.html
Datapath | Holds and shifts the four-bit word. | Contains the register and bit count.
Controller | Chooses IDLE, LOAD, SHIFT, DONE. | Generates load, shift and done controls.

## Slide 12
L24 · INTERACTIVE COMPANION
Serial transmitter walkthrough
Textbook: Review Ch. 6–9 and Ch. 5 §5.6
ELEC 335 | L24 | Week 13
12
IDLE
→
LOAD
→
SHIFT
→
DONE
Controller states select datapath microoperations
Load a four-bit word, start the controller and advance each clock edge. State, count, data and emitted bits animate together.
Open lesson-10.html for the animated model and state-by-state controls.
Notes: ELEC 335 | Lecture 24 | Week 13
Interactive model
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Review Ch. 6–9 and Ch. 5 §5.6.
Companion animation: lesson-10.html
Load a four-bit word, start the controller and advance each clock edge. State, count, data and emitted bits animate together.
Invite students to predict the next state before every edge.
Write emitted bits on the board and compare with the changing register.
End by asking learners to map the controller table to a ROM word format.

## Slide 13
ACTIVITY
L24
TEAM
TASK
Apply the method together
Design the control outline for a four-bit serial transmitter. Show when load, shift and done are asserted, including a new start request.
Separate controller state, datapath registers, inputs, and observable outputs.
DELIVERABLE
A state diagram, register actions and a concise verification trace.
Textbook: Review Ch. 6–9 and Ch. 5 §5.6
L24 | Week 13
ELEC 335 | Digital Logic Design
13
Notes: ELEC 335 | Lecture 24 | Week 13
Team activity
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Review Ch. 6–9 and Ch. 5 §5.6.
Companion animation: lesson-10.html
Design the control outline for a four-bit serial transmitter. Show when load, shift and done are asserted, including a new start request.
Deliverable: A state diagram, register actions and a concise verification trace.

## Slide 14
L24 · GUIDED EXAMPLE
Try the first move before I do
Textbook: Review Ch. 6–9 and Ch. 5 §5.6
ELEC 335 | L24 | Week 13
14
Use a two-bit state code and two condition bits (start, last) as a conceptual controller address. Store two next-state bits and three action bits.
YOUR FIRST MOVE
There are 2⁴=16 possible addresses.
Pause for 60–90 seconds. Write, then compare with a partner.
Notes: ELEC 335 | Lecture 24 | Week 13
Guided example
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Review Ch. 6–9 and Ch. 5 §5.6.
Companion animation: lesson-10.html
Prompt: Use a two-bit state code and two condition bits (start, last) as a conceptual controller address. Store two next-state bits and three action bits.
First move: There are 2⁴=16 possible addresses.
Pause before showing the next slide.

## Slide 15
L24 · GUIDED SOLUTION
Now make every step visible
Textbook: Review Ch. 6–9 and Ch. 5 §5.6
ELEC 335 | L24 | Week 13
15
1
There are 2⁴=16 possible addresses.
2
Each word contains 2+3=5 output bits.
3
The conceptual ROM organization is 16×5.
4
Specify all unused address words, including invalid state encodings if any, for safe behavior.
The organization is 16×5, or 80 stored output bits. Conditions must be defined for every address.
Notes: ELEC 335 | Lecture 24 | Week 13
Estimate a ROM for the controller
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Review Ch. 6–9 and Ch. 5 §5.6.
Companion animation: lesson-10.html
Steps:
There are 2⁴=16 possible addresses.
Each word contains 2+3=5 output bits.
The conceptual ROM organization is 16×5.
Specify all unused address words, including invalid state encodings if any, for safe behavior.
Answer: The organization is 16×5, or 80 stored output bits. Conditions must be defined for every address.

## Slide 16
L24 · MISCONCEPTION CLINIC
A tempting mistake to remove now
Textbook: Review Ch. 6–9 and Ch. 5 §5.6
ELEC 335 | L24 | Week 13
16
TEMPTING CLAIM
The register operation can be decided without specifying controller timing.
WHY IT FAILS
Load, shift and done must occur in defined states and clock intervals.
REPAIR
Write a state table with actions and verify the edge-by-edge trace.
Notes: ELEC 335 | Lecture 24 | Week 13
Misconception clinic
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Review Ch. 6–9 and Ch. 5 §5.6.
Companion animation: lesson-10.html
TEMPTING CLAIM: The register operation can be decided without specifying controller timing.
WHY IT FAILS: Load, shift and done must occur in defined states and clock intervals.
REPAIR: Write a state table with actions and verify the edge-by-edge trace.

## Slide 17
L24 · ONE-MINUTE CHECKS
Close the book: can you apply it?
Textbook: Review Ch. 6–9 and Ch. 5 §5.6
ELEC 335 | L24 | Week 13
17
Q1
If a PISO register holds 0110 and emits the rightmost bit first, what is the output sequence?
Q2
Why does the controller need a count as well as the data register?
Answer without notes, then compare your reasoning with the next slide.
Notes: ELEC 335 | Lecture 24 | Week 13
Practice questions
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Review Ch. 6–9 and Ch. 5 §5.6.
Companion animation: lesson-10.html
Q1: If a PISO register holds 0110 and emits the rightmost bit first, what is the output sequence?
Hint: Read bits from right to left.
Answer: 0,1,1,0.
Q2: Why does the controller need a count as well as the data register?
Hint: The data pattern itself may contain zeros and ones.
Answer: The count records how many bits remain; data bits alone do not indicate whether four transfers have occurred.

## Slide 18
L24 · PRACTICE SOLUTIONS
Check the rule behind each answer
Textbook: Review Ch. 6–9 and Ch. 5 §5.6
ELEC 335 | L24 | Week 13
18
Q1
0,1,1,0.
Q2
The count records how many bits remain; data bits alone do not indicate whether four transfers have occurred.
Return to the reference table if your answer used a different rule.
Notes: ELEC 335 | Lecture 24 | Week 13
Practice solutions
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Review Ch. 6–9 and Ch. 5 §5.6.
Companion animation: lesson-10.html
Q1: If a PISO register holds 0110 and emits the rightmost bit first, what is the output sequence?
0,1,1,0.
Q2: Why does the controller need a count as well as the data register?
The count records how many bits remain; data bits alone do not indicate whether four transfers have occurred.

## Slide 19
L24 · CLOSE
What should stay with you
Textbook: Review Ch. 6–9 and Ch. 5 §5.6
ELEC 335 | L24 | Week 13
19
Model a small serial transmitter as an FSM
Trace parallel load and serial shift timing
Map a controller table to ROM or product terms
NEXT
Review the design methods and test each circuit against its full state table.
Notes: ELEC 335 | Lecture 24 | Week 13
Closing outcomes
Reading: Alan B. Marcovitz, Introduction to Logic Design, 3rd ed., Review Ch. 6–9 and Ch. 5 §5.6.
Companion animation: lesson-10.html
Model a small serial transmitter as an FSM
Trace parallel load and serial shift timing
Map a controller table to ROM or product terms
Next companion: course review